## Slide 1: WF on multi-panel codebook extension
Ericsson, Samsung, Huawei, HiSilicon,…
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21st – 25th August, 2017
Agenda item 6.2.2.3
R1-1714906

## Slide 2: Background
The following configurations of number of panels and panel port layouts are supported for the Type I multi-panel codebook:
Thus, the case with two ports per panel (i.e. one port per panel and polarization), , is not supported.
Number of CSI-RS ports |  | 
8 | (2,2,1) | (4,-)
16 | (2,2,2) | (4,4)
 | (2,4,1), (4,2,1) | (4,-)
32 | (2,4,2), (4,2,2) | (4,4)
 | (2,8,1), (4,4,1) | (4,-)
Number of CSI-RS ports |  | 
8 | (2,2,1) | (4,-)
16 | (2,2,2) | (4,4)
 | (2,4,1), (4,2,1) | (4,-)
32 | (2,4,2), (4,2,2) | (4,4)
 | (2,8,1), (4,4,1) | (4,-)

## Slide 3: Proposal
The Type I multi-panel codebook supports the two additional port/panel combinations , i.e. 2 ports per panel is supported for 2 and 4 panels
  Both mode 1 and mode 2 are supported for and rank 1-4
  For the rank-1 and rank-2 codebook, existing codebook formulation is reused
  For the rank-3 and rank-4 codebook, study further and downselect between the following alternatives:
    Alt.1: Precoders implement non-coherent transmission from groups of panels
      For instance:
    Alt. 2: Precoders implement coherent transmission from all panels
      For instance:
    Alt. 3: Use single-panel rank-3 / 4 codebook
    Other options are not precluded