## Slide 1: Way forward on reciprocity based CSI
ZTE, Ericsson, Samsung, LG Electronics, Nokia, NSB
3GPP TSG RAN WG1 Meeting #90 R1-1714907
Prague, Czechia 21st – 27th August 2017
Agenda Item: 6.1.2.2.2

## Slide 2: Background
  At least for full channel reciprocity, support at least the following CSI acquisition scheme based on channel reciprocity in NR
    Non-PMI feedback
      CSI contains RI and CQI
      CQI depends on RI and PMI which are selected from a codebook (potentially with restriction) but PMI is not fed back
        FFS UE may also calculate RI and CQI directly with estimated channel, FFS spec impact
    FFS codebook details, including how to signal
  For non-PMI feedback, the following agreement has been reached in RAN1#88bis:

## Slide 3: Proposal
  Port selection codebook is used for CQI calculation for non-PMI feedback
    Each column of each precoding matrix in the port selection codebook contains only one non-zero entry
      FFS other details of the port selection codebook
    Codebook subset restriction is supported to indicate a single precoder per rank in the codebook used for CQI calculation
      FFS whether this indication can be dynamic using L1/L2 signaling
    Support at least up to 8 CSI-RS ports and 8 layers