## Slide 1: WF on group-based beam reporting
3GPP TSG RAN WG1 Meeting #90 R1-1714909
Prague, Czechia, 21st – 25th August 2017
Agenda Item: 6.1.2.2.4
ZTE, Samsung, NTT DOCOMO, Huawei, HiSilicon, vivo, [Nokia, ASB, CATT, Qualcomm, MediaTek, Ericsson, Intel, OPPO, LGE]

## Slide 2: Background
  The following agreements on group-based beam reporting been reached:
    Alt 1:
  - UE reports information about TRP Tx Beam(s) that can be received using selected UE Rx beam set(s) where a Rx beam set refers to a set of UE Rx beams that are used for receiving a DL signal.
    - NOTE: Different TRP Tx beams reported for the same Rx beam set can be received simultaneously at the UE.
    - NOTE: Different TRP TX beams reported for different UE Rx beam set may not be possible to be received simultaneously at the UE
Alt 2:
  - UE reports information about TRP Tx Beam(s) per UE antenna group basis where UE antenna group refers to receive UE antenna panel or subarray.
    - NOTE: Different TX beams reported for different antenna groups can be received simultaneously at the UE.
    NOTE: Different TX beams reported for the same UE antenna group may not be possible to be received simultaneously at the UE

## Slide 3: Background
  The following agreements on details of group-based beam reporting have been reached:
  NR supports the following beam reporting considering L groups where L>=1 and each group refers to a Rx beam set (Alt1) or a UE antenna group (Alt2) depending on which alternative is adopted.
  For each group l, UE reports at least the following information:
    Information indicating group at least for some cases
      FFS: condition(s) to omit this parameter e.g. when L=1 or Nl=1
    Measurement quantities for Nl beam (s)
      Support L1 RSRP and CSI report (when CSI-RS is for CSI acquisition)
        FFS: the details of RSRP/CSI derivation and content
        FFS: Other reporting contents, e.g., RSRQ
        FFS: Configurability between L1 RSRP and CSI report
        FFS: whether or not to support differential L1 RSRP feedback
        FFS: How to select Nl beam(s) e.g max Nl beams in terms of received power being above a certain threshold or in terms of correlation less than a certain threshold
    Information indicating Nl DL Tx beam(s) when applicable
      FFS: the details on this information, e.g., CSI-RS resource IDs, antenna port index, a combination of antenna port index and a time index, sequence index, beam selection rules for assisting rank selection for MIMO tx, etc.
  This group based beam reporting is configurable per UE basis.
    This group based beam reporting can be turned off per UE basis e.g. when L=1 or Nl=1
      NOTE: No group identifier is reported when it is turned off
    FFS: how L is determined. e.g. by network configuration or UE selection or UE capability e.g. how many beams can be received simultaneously
    FFS: how is configured using the CSI framework to support multi-panel or multi-TRP transmission

## Slide 4: Proposal
  Support the following the group based beam reporting, if the group based beam reporting is turned on:
    In a beam reporting instance, a UE can be configured to report N different Tx beams that can be received simultaneously
      N<=Nmax, where Nmax is configured by the gNB
    Note:
      For the perspective of Alt-1, the UE reports one group with N Tx beams.
      For the perspective of Alt-2, the UE reports N group with one Tx beam per each group.