## Slide 1: WF on Non-Codebook based UL Transmission
Huawei, HiSilicon, DOCOMO, Ericsson, InterDigital, LGE, Sharp, China Telecom, ZTE, Sanechips, Nokia, NSB, AT&T, China Unicom, Spreadtrum, Fujitsu, CeWiT, Intel, IITM, Mitsubishi, MediaTek, Lenovo, IITH, Tejas Networks, CATT
3GPP TSG RAN WG1 NR Ad Hoc Meeting R1-1714945
Prague, Czech Republic, 21 – 25 August 2017
Agenda item – 6.1.2.1.3

## Slide 2: Backgroud
In last meeting, there are following agreements:
Agreements:
For PUSCH precoder determination in non-codebook-based UL MIMO, support at least one of the followings:
  Alt.1: Signalling of SRI(s) only, without TPMI indication in the UL grant
  Alt.2: Signalling of TRI only, without TPMI indication in the UL grant
  Alt.3: Signalling of TRI and a single SRI, without TPMI indication in the UL grant
  Alt. 4: signalling of a single TRI, a single CRI without TPMI indication in the UL grant
  To down-select in the next meeting considering single- vs. multi-panel (companies are encouraged to perform more evaluations)
  Note: this may depend UE’s capability in terms of calibration

## Slide 3: Proposals
  For PUSCH precoder determination in non-codebook-based UL MIMO, support Alt.1, (i.e., at least SRI(s) only without TPMI indication in the UL grant) for wideband indication.
    Note: the network is aware what precoded transmissions inferred from SRS transmission(s) can be simultaneously conducted by the UE.
    FFS signaling and/or configuration details
    FFS: If sub-band indication is supported, down-select Alt. 1-3 for it