## Slide 1: Way Forward for the Numerology in NR RA Procedures
CATT, [….],
3GPP TSG RAN WG1#90 R1-1714963
Prague, Czech Republic, 21st – 25th August 2017
Agenda 6.1.1.4.4

## Slide 2: Background
A contention-based RA procedure involves following 4-steps
  Msg1: Random Access Preamble on RACH in uplink
  Msg2: Random Access Response generated by MAC on DL-SCH
  Msg3: First scheduled UL transmission on UL-SCH
  Msg4: Contention Resolution on DL
A non-contention based random access procedure includes 3-steps:
  Msg0: Random Access Preamble assignment via dedicated signalling in DL (e.g., Handover command)
  Msg1: Random Access Preamble on RACH in uplink
  Msg2: Random Access Response on DL-SCH
Different numerologies may be used in the RACH messages in 4-steps and 3-steps RA procedures.

## Slide 3: Background (cont.)
Options for the subcarrer spacing for contention-based NR 4-step RA Procedure
    Msg1:
      configured in the RACH configuration
    Msg2:
      Option 1: the same as SCS in PBCH transmission
      Option 2: configured in RACH configuration in RMSI
      Option 3: the same as SCS in RMSI transmission
    Msg3:
      Option 1: the same as SCS in PBCH transmission
      Option 2: configured in RACH configuration
      Option 3: indicated in RAR (Msg.2)
      Option 4: the same as SCS in RMSI transmission
    Msg4:
      Option 1: the same as SCS in PBCH transmission
      Option 2: configured in RACH configuration
      Option 3: the same as SCS in Msg.2
      Option 4: the same as SCS in RMSI transmission

## Slide 4: Background (cont.)
Options for the subcarrer spacing for contention-free NR 3-step RA Procedure
    Msg1:
      Option 1: the same as the SCS of Msg.0 from source cell
      Option 2: configured in RACH configuration in Msg.0
    Msg2:
      Option 1: the same as the SCS of Msg.0 from source cell
      Option 2: configured in RACH configuration in Msg.0
      Option 3: the same as the SCS in SS blocks of the target cell if the HO is triggered by the SS-RSRP measurement, or the same as the SCS in CSI-RS of the target cell if the HO is triggered by the CSI-RS RSRP

## Slide 5: Proposal
For contention-based NR 4-step RA procedure
  SCS for Msg 1
    configured in the RACH configuration
  SCS for Msg 2
    For RRC_IDLE mode UE
      the same as used in RMSI transmission
    For RRC_CONNECTED mode UE
      the same as the numerology of the active DL bandwidth part
  SCS for Msg 3
    For RRC_IDLE UE mode UE
      the same as used in RMSI transmission by default, unless it is configured in the RACH configuration in RMSII
    For RRC_CONNECTED mode UE :
      the same as the numerology of the active UL bandwidth part
  SCS for Msg 4
    the same as in Msg.2

## Slide 6: Proposal
For contention-free 3-step RA procedure
  SCS for Msg 1
    provided in the RACH configuration in the DL signaling (Msg. 0)
  SCS of Msg 2
    For a non-handover procedure
      the same as the SCS in Msg.0 by default, unless it is reconfigured by Msg. 0.
    For a handover procedure,
      configured by the DL signaling (Msg. 0), or
      the same SCS (e.g., CSI-RS or SS) as the reference signal of the target cell which triggers the handover event.