## Slide 1: Assumptions for eMTC power consumption for power saving signal/channel
Ericsson
3GPP TSG-RAN WG1 Meeting #90 R1-1714992
Prague, Czech Republic, 21st – 25th August 2017
Agenda item 5.2.6.2

## Slide 2: UE assumptions
Parameter | Value
LO XO frequency drift [ppm/s] | 0.05
LO XO max frequency error [ppm] | 5
RTC max frequency error [ppm] | 20
The relationship between a frequency error, Fe, and corresponding timing drift, ΔT, over a time, T, is ΔT = ±Fe * T (saturated region)
The relationship between a frequency drift, F’, and corresponding timing drift, ΔT, over a time, T, is ΔT = ±0.5 * F’ * T2 (transient region)
The RTC is assumed to be uncalibrated with LO XO, i.e., to operate in the saturated region
Note: The above parameters apply only to some architectures. It does not mean all the UEs will support it.
Operating mode | Power [units/ms] | Total ramp up or ramp down time [ms] | Notes
Idle, deep sleep | 0.015/[0.05] |  | Deep sleep during PSM and eDRX, depending on UE architecture.
Transitions to or from deep sleep | 50 | 200/[25] | Boot, reload memory etc., depending on UE architecture.
Transitions to or from light sleep | 50 | 15 | Boot, reload memory etc.

## Slide 3: efeMTC assumptions
Scenario | A | B | C
eDRX cycle [s] | - | 20.48 | 327.68
DRX cycle [s] | 2.56 | 0.32 | 0.32
#POs/PTW | 1 | 4 | 4
Paging rate [%] | 10 | 10 | 10
Other scenarios are not precluded
Paging rates < 10% are encouraged to show the potential gain of the power saving signals
Timing drift is computed according to the above relationships between frequency error or frequency drift and T is the time from the previous synchronization. T may take different values depending on the chosen synchronization approach and paging rate, Ppaging, e.g.,
  WUS+DTX: T = T(e)DRX / Ppaging
  WUS+GTS: T = T(e)DRX
  Other synchronization approaches are not precluded
Ppaging is the probability of receiving a Paging message in any PO (within a PTW) and where paging in POs appear with equal probability
Resynchronization assumptions and resulting power costs should be included in the assessment
SIBs are assumed to be valid throughout the assessment
Erroneous detections:
  WUS misdetection rate <1%
  WUS false alarm impact (for up to ±5 ppm frequency errors when not relying on DL synchronization) should be included in power consumption evaluation result
  WUS false alarm impact from other DL transmission should be included in power consumption evaluation result
  The above cases should be evaluated for both AWGN and ETU 1
The following should be described:
  Information conveyed by the physical signal
  Design of the physical signal
Impacts from RRM mobility measurements are FFS

## Slide 4: efeMTC
For idle mode,
  The power saving signal in a cell supports being applied to FFS between:
    (a): All the UEs associated to a PO in the cell
    (b): A group of more than one of the UEs associated to a PO in the cell
    Both (a) and (b)
  How many POs the power saving signal applies to from the UE perspective is FFS between
    A single PO only
    One or more than one PO (details are FFS)
  How many POs the power saving signal applies to from the eNB perspective is FFS between
    A single PO only
    One or more than one PO (details are FFS)
The following bullet provides a common basis for simulation purposes, however the issue will be discussed in RAN1#90bis:
  The power saving signal applicable to a UE is sent on the same narrowband as the first subframe of the associated subsequent physical channel(s) for Paging

## Slide 5: Appendix R1-1706704+R1-1714992

## Slide 6: Metrics and simulations assumptions
  To evaluate the techniques for Downlink channel power efficiency the following assumptions are proposed:
    Performance metrics:
      Other metrics are not precluded.
      See next slides for detailed assumptions on power efficiency evaluations.
    Simulation assumptions:
      Other assumptions important for achieved performance such as use of cross-subframe channel estimation should be declared.
Performance Metric | Unit
Power efficiency | % (reduced power consumption)
Miss detection rate | % (expressed as 100 – percentage of successful detection events)
False detection rate | % (expressed as percentage of false detection events)
System overhead | % (expressed as used part of all REs per radio frame)
Parameter | Value
BS TX antenna configuration | 2 Tx
BS power | 43 dBm per TX port
System BW | 10 MHz
Band | Band 8 (900 MHz)
Channel model | ETU
Doppler spread | 1 Hz
LO XO frequency drift, when not relying on DL synchronization (light sleep) | ±0.05 ppm/s
LO XO maximum frequency error, when not relying on DL synchronization (light sleep) | ±5 ppm
LO XO frequency error, when relying on DL synchronization (receive) | ±30 Hz
RTC maximum frequency error (medium, deep sleep) | ±20 ppm
UE RX antenna configuration | 1 Rx
UE NF | 9 dB
Coupling loss | 144, 154, 164 dB

## Slide 7: Power efficiency
Reference power consumption model:
The proponent of candidate technologies should declare the assumed power model used in the evaluations of the candidate technology
Note: A unit of power is not defined to be the same between NB-IoT and eMTC
Note: The above parameters apply only to some architectures. It does not mean all the UEs will support it.
Operating mode | Power [units/ms] | Total ramp up or ramp down time [ms] | Notes
Receive | 100 |  | RF and baseband circuitry.
Light sleep | 1 |  | Corresponds to maintaining accurate timing by keeping RF frequency reference active.
Idle, deep sleep | 0.015/[0.05] |  | Deep sleep during PSM and eDRX, depending on UE architecture.
Transitions to or from light sleep | 50 | 15 | Boot, reload memory etc.
Transitions to or from deep sleep | 50 | 200/[25] | Boot, reload memory etc., depending on UE architecture.

## Slide 8: Power efficiency
The UE power consumption at PSS/SSS (when applicable), PBCH (when applicable) MPDCCH reception should be evaluated for one or more of the following scenarios:
  Idle mode and/or Connected mode
  eDRX and/or DRX, with assumed DRX cycle declared.
  These assumptions will impact the modeled time/frequency drift (see table on slide 3).
The reference scenario is a UE that monitors the MPDCCH transmission, but is not receiving a PDSCH. This includes both idle and connected mode. In idle mode a page for another UE is present in 0% and X % of the cases.
  The power consumption PREF for the reference scenario should be calculated and used as baseline in the evaluations.
  X should be reported.
  Simple example for connected mode:
    Assumptions: 164 dB coupling loss, Connected mode with freq. error of 30 Hz, The UE ramps up from light sleep to decode a single MPDCCH transmission and then ramps down to light sleep.
The impact on power consumption from adding the candidate solution to the reference scenario should be evaluated and reported.
  The power consumption PCANDIDATE when implementing the candidate technique should be calculated
The metric to report is PCANDIDATE/PREF
Activity | Cost | Comment
Ramp up from light sleep | 50 units/ms * 15 ms = 750 units | Assuming 50 units/ms during 15 ms
Sync | 100 unit/ms * 2 ms = 200 units | Sync
Decode MPDCCH | 100 units/ms * 64 ms = 6400 units | Assuming 64 MPDCCH repetitions.
Ramp down to light sleep | 50 units/ms*15 ms = 750 units | Assuming 50 units/ms during 15 ms
PREF | 8100 units | Reference power consumption