## Slide 1: Way Forward on Rate-Matching for Polar Code
MediaTek, Qualcomm, Samsung, ZTE
R1-1715000
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21st - 25th August 2017
Agenda item 6.1.4.2.3

## Slide 2: Background (1/2)
Next Steps:
Companies to work together this evening on a single (i.e. single scheme for UL, DL and all rates / sizes) merged rate matching proposal
Evaluate BLER performance (with further iterations of the design if necessary) until Friday morning.
On Friday morning, take a Working Assumption on a single rate matching design (the merged proposal if possible, otherwise one or more alternatives from the other known schemes; if more than one scheme ends up in the working assumption, note that this will multiply the needed FAR evaluations).
The Working Assumption Rate Matcher will be used in the FAR evaluations for the code construction.

## Slide 3: Background (2/2)
Rate-matching proposals:
  Bit-level interlacing based design:
    MediaTek: Middle interlacing (R1-1713705)
  Subblock-wise interleaving based designs:
    Samsung: 16-subblock interleaving (R1-1714179)
    ZTE: 32-subblock interlaving (R1-1714939)
  Information allocation based design
    Qualcomm: Block Rate-Matching with Information Allocation Adjustment (BRMIAA; R1-1713470)
The companies work together for a single design with enhanced performance

## Slide 4: Rate-Matching Option 1 (1/8)
Characteristics:
  Performance prioritized design
  Subblock-wise middle interlacing and interleaving with 32 subblocks and information allocation adjustment for enhanced performance
  Bit pre-freezing for stabilized list-1 performance

## Slide 5: Rate-Matching Option 1 (2/8)
Encoder output processing
  Rate-matching interleaving
    Subblock-wise middle interlacing and interleaving with 32 size-N/32 subblocks
    Output order: 0 1 2 3 4 5 6 7 8 9 10 11 12 16 13 17 14 18 15 19 20 24 21 22 25 26 28 23 27 29 30 31
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 25 | 27 | 28 | 29 | 30 | 31
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 16 | 13 | 17 | 14 | 18 | 15 | 19 | 20 | 24 | 21 | 22 | 25 | 26 | 28 | 23 | 27 | 29 | 30 | 31

## Slide 6: Rate-Matching Option 1 (3/8)
Encoder output processing (Cont’d)
  Circular buffer access:
    Puncturing is realized by selecting bits from position (N-M) to position (N-1) from the circular buffer
    Shortening is realized by selecting bits from position 0 to position M-1 from the circular buffer
    Repetition is realized by selecting all bits from the circular buffer, and additionally repeat (M-N) consecutive bits with the smallest index bit from the circular buffer
  Selection of the rate-matching mode among puncturing, shortening and repetition, follows the rule next page.

## Slide 7: Rate-Matching Option 1 (4/8)
After segmentation (if any):
K is the number of information bits (including CRC if one is attached)
M is the number of coded bits for transmission
NDM is the smallest power of 2 that is >=M
NM is
  NDM /2 if M < β* NDM /2 and K/M <= 1/3, β = 1+1/16
  Otherwise, NDM
NR is the smallest power of 2 that is >= K/Rmin
  Rmin = 1/8 is the supported minimum coding rate,
Nmax is the maximum supported mother code size
The mother code size N is determined as min(NM, NR, Nmax)
Repetition is applied when M > N, and no IAA is applied, i.e., J = 0
Puncturing or shortening is applied when M < N
  Puncturing for K/M <= 0.45; shortening otherwise

## Slide 8: Rate-Matching Option 1 (5/8)
Encoder input processing:
  Information Allocation Adjustment (IAA)
    Compute the J value, where J is the non-punctured bits in the upper part for puncture and non-shortened bits in the lower part for shorten:
      M >= 3N/4, No IAA, = (M – N/2)
      (5/8 – 1/32) N <= M < 3N/4, = (M – N/2)
      (5/8 – 2/32) N <= M < (5/8 – 1/32) N, = 3N/32
      (5/8 – 3/32) N <= M < (5/8 – 2/32) N, = M – 15N/32
      (5/8 – 4/32) N <= M < (5/8 – 3/32) N, = N/16
    / computation:
      : Number of the information bits allocated to upper half of Polar encoder input
      : Number of the information bits allocated to upper half of Polar encoder input
      Computation can be done by a predetermined table according to the following formula. An example table is also attached.

## Slide 9: Rate-Matching Option 1 (6/8)
Encoder input processing (Cont’d):
  Bit pre-freezing
    Freeze all input bits corresponding to untransmitted coded bits
    For puncturing, additionally freeze any unfrozen bit with index

## Slide 10: Rate-Matching Option 1 (7/8)
Performance comparison (list-1)

## Slide 11: Rate-Matching Option 1 (8/8)
Performance comparison (list-8)

## Slide 12: Rate-Matching Option 2 (1/7)
Characteristics:
  Performance and complexity balanced design
  Subblock-wise middle interlacing and interleaving with 32 subblocks for enhanced performance
  Bit pre-freezing for stabilized list-1 performance

## Slide 13: Rate-Matching Option 2 (2/7)
Encoder output processing
  Rate-matching interleaving
    Subblock-wise middle interlacing and interleaving with 32 size-N/32 subblocks
    Output order: 0 1 2 4 3 5 6 7 8 16 9 17 10 18 11 19 12 20 13 21 14 22 15 23 24 25 26 28 27 29 30 31
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 25 | 27 | 28 | 29 | 30 | 31
0 | 1 | 2 | 4 | 3 | 5 | 6 | 7 | 8 | 16 | 9 | 17 | 10 | 18 | 11 | 19 | 12 | 20 | 13 | 21 | 14 | 22 | 15 | 23 | 24 | 25 | 26 | 28 | 27 | 29 | 30 | 31

## Slide 14: Rate-Matching Option 2 (3/7)
Encoder output processing (Cont’d)
  Circular buffer access:
    Puncturing is realized by selecting bits from position (N-M) to position (N-1) from the circular buffer
    Shortening is realized by selecting bits from position 0 to position M-1 from the circular buffer
    Repetition is realized by selecting all bits from the circular buffer, and additionally repeat (M-N) consecutive bits with the smallest index bit from the circular buffer
  Selection of the rate-matching mode among puncturing, shortening and repetition, follows the rule next page.

## Slide 15: Rate-Matching Option 2 (4/7)
After segmentation (if any):
K is the number of information bits (including CRC if one is attached)
M is the number of coded bits for transmission
NDM is the smallest power of 2 that is >=M
NM is
  NDM /2 if M < β* NDM /2 and K/M < 9/16, β = 1+1/8
  Otherwise, NDM
NR is the smallest power of 2 that is >= K/Rmin
  Rmin = 1/8 is the supported minimum coding rate,
Nmax is the maximum supported mother code size
The mother code size N is determined as min(NM, NR, Nmax)
Repetition is applied when M > N
Puncturing or shortening is applied when M < N
  Puncturing for K/M <= 0.7/16; shortening otherwise

## Slide 16: Rate-Matching Option 2 (5/7)
Encoder input processing:
  Bit pre-freezing
    Freeze all input bits corresponding to untransmitted coded bits
    For puncturing, additionally freeze any unfrozen bit with index where
    No additional bit freezing for shortening or repetition.

## Slide 17: Rate-Matching Option 2 (6/7)
Performance comparison (list-1)

## Slide 18: Rate-Matching Option 2 (7/7)
Performance comparison (list-8)

## Slide 19: Proposal
RAN1 adopt the merged rate-matching option 1 as the working assumption for Polar rate-matching

## Slide 20: More performance results of option 1

## Slide 21: Qualcomm (1/2)
Performance comparison (list-1)

## Slide 22: Qualcomm (2/2)
Performance comparison (list-8)

## Slide 23: ZTE (1/2)

## Slide 24: ZTE (2/2)