## Slide 1: WF on intra-collision avoidance for AUL UEs
Ericsson, NOKIA, …
R1-1715005
3GPP TSG RAN1 #90
Prague, Czech Republic, 21st– 25th Aug 2017
Agenda item 5.2.2.3.3

## Slide 2: Background
At low load, where latency matters the most, there are benefits from assigning same AUL time resources to different UEs.
However, if common starting position is used, there is a chance that multiple AUL UEs start simultaneous transmission and collide.
To reduce intra-cell collisions, the eNB can spread out the earliest possible transmission time for AUL UEs. (Figure 1 provides an example). This will give the UEs different priority to access the channel.
To minimize eNB blind decoding according to different starting positions, the PUSCH starting position is aligned for different AUL UEs.
  CP extension is used for transmissions before the next allowed transmission boundary where the PUSCH transmission starts.

## Slide 3: Proposal
The PUSCH starting position is configured by the eNB.
  FFS: supported starting positions, e.g. OS#0 and OS#1
AUL operation supports indication of UE-specific transmission starting position.
  FFS: if RRC configured
CP extension is used for transmissions before the next allowed transmission boundary where the PUSCH transmission starts.