## Slide 1: WF on Spatial QCL Relation Signaling
Samsung
R1-1715006
3GPP TSG RAN WG1 #90
Prague, Czech, 21 – 25 Aug 2017
Agenda item 6.1.2.3.7

## Slide 2
RAN1 AH1 Agreements:
Indication of QCL between the antenna ports of two CSI-RS resources is supported.
  By default, no QCL should be assumed between antenna ports of two CSI-RS resources.
  Partial QCL parameters (e.g., only spatial QCL parameter at UE side) should be considered.
For downlink, NR supports CSI-RS reception with and without beam-related indication,
  When beam-related indication is provided, information pertaining to UE-side beamforming/receiving procedure used for CSI-RS-based measurement can be indicated through QCL to UE
  QCL information includes spatial parameter(s) for UE side reception of CSI-RS ports
    FFS: information other than QCL

## Slide 3: Background
RAN1#89 Agreements:
Support spatial QCL assumption between antenna port(s) within a CSI-RS resource(s) and antenna port of an SS Block (or SS block time index) of a cell
  The other QCL parameters not precluded
  FFS: indication either explicit or implicit or configurable or a default
  Note: default assumption may be no QCL
Configuration of QCL for UE specific NR-PDCCH is by RRC and MAC-CE signalling
  Note that MAC-CE is not always needed
  FFS: necessity of DCI signalling
  Note: For example, DL RS QCLed with DMRS of PDCCH for delay spread, Doppler spread, Doppler shift, and average delay parameters, spatial parameters

## Slide 4: Proposal
Note: The indicator state referred in below text is defined in R1-1714885
Following ways of configuring QCL relations between a reference RS and a targeted RS are supported
  If configured, at least spatial QCL relation between SS Block and P/SP CSI-RS is signaled by RRC
  If configured, at least spatial QCL relation between a P/SP CSI-RS resource and another (different) P/SP CSI-RS resource is signaled by RRC
  At least spatial QCL relation for an AP CSI-RS resource is provided through an indicator state in the DCI message which triggers that resource.
    E.g. to indicate QCL relation between AP CSI-RS and a SSB/P/SP CSI-RS resource Y, the DCI message provides the indicator state associated with Y.
  FFS : Other candidate relations
Association between an indicator state and P/SP CSI-RS index can be done via RRC + MAC CE signaling implicitly/explicitly

## Slide 5: Table Summary
Following ways of configuring spatial QCL relations between RS are supported
Association between indicator state and P/SP CSI-RS index can be done via RRC + MAC CE signaling implicitly/explicitly
Target RS | Reference RS | Method of Signaling
P/SP CSI-RS | SS Block | RRC
P/SP CSI-RS2 | P/SP CSI-RS1 | RRC
AP CSI-RS | P/SP CSI-RS or SSB | Indicator state (associated with index of P/SP CSI-RS) in DCI triggering AP CSI-RS
AP CSI-RS 2 | AP CSI-RS 1 | Indicator state (associated with index of AP CSI-RS1) in DCI triggering AP CSI-RS 2

## Slide 6: Reference
Ref: R1-1710663
Ref: R1-1710664