## Slide 1
3GPP TSG RAN WG1 Meeting #90 R1-1715029
Prague, Czech Republic, 21-25 August 2017
Agenda Item: 6.1.1.1.1
WF on SS burst set mapping into radio frame
Huawei, HiSilicon

## Slide 2: Background
  In RAN1 AdHoc meeting in June,
    The SS burst set composition in terms of mapping of SS blocks to slots have been finalized.
    However, it was noted in the agreement that for NR and LTE coexistence, duplex direction alignment can be achieved by subframe offset.
  It was agreed in RAN1#87 that
    For adjacent channel/band operation of NR and LTE in the unpaired spectrum,
      Design at least one semi-statically assigned DL/UL transmission direction configuration for NR that avoids DL/UL interference with at least one LTE TDD DL/UL configuration and special subframe configuration

## Slide 3: Background
(a) 15KHz
(b) 30KHz
SSB mapping pattern in NR for 15kHz and 30kHz

## Slide 4: Background
UL/DL configurations in LTE
If an SS burst set is mapped over a UL subframe, a large number of SSBs can not be transmitted.
To ensure full mapping of the SSBs per SS burst set within a frame, NR should strive to map the SS burst set taking into account the DL/UL configurations
Uplink-downlink configuration | Downlink-to-Uplink Switch-point periodicity | Subframe number |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 5 ms | D | S | U | U | U | D | S | U | U | U
1 | 5 ms | D | S | U | U | D | D | S | U | U | D
2 | 5 ms | D | S | U | D | D | D | S | U | D | D
3 | 10 ms | D | S | U | U | U | D | D | D | D | D
4 | 10 ms | D | S | U | U | D | D | D | D | D | D
5 | 10 ms | D | S | U | D | D | D | D | D | D | D
6 | 5 ms | D | S | U | U | U | D | S | U | U | D

## Slide 5: Proposal
To facilitate NR-LTE coexistence, NR supports Subframe Offset of the SS burst set mapping onto the radio frame.
  FSS: Identify applicable DL/UL configurations and its associated subframe offset.

## Slide 6: Example: Possible configuration and subframe offset values
UL/DL configuration | SS burst set position (i.e., N+Δ) |  |  | 
 | Subframe number (N) | Subframe offset (Δ) | Subframe number (N) | Subframe offset (Δ)
2 | 0 | -2 | 5 | -2
4 | 0 | -2 | 5 | -1
5 | 0 | -2, -3 | 5 | -2
Uplink-downlink configuration | Downlink-to-Uplink Switch-point periodicity | Subframe number |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 5 ms | D | S | U | U | U | D | S | U | U | U
1 | 5 ms | D | S | U | U | D | D | S | U | U | D
2 | 5 ms | D | S | U | D | D | D | S | U | D | D
3 | 10 ms | D | S | U | U | U | D | D | D | D | D
4 | 10 ms | D | S | U | U | D | D | D | D | D | D
5 | 10 ms | D | S | U | D | D | D | D | D | D | D
6 | 5 ms | D | S | U | U | U | D | S | U | U | D