## Slide 1: WF on RMR types
LG Electronics, Intel, ZTE, NTT DOCOMO
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21st – 25th August 2017
Agenda item: 6.1.2.1.7
R1-1715034

## Slide 2: Background
In RAN1 Ad-hoc #2 meeting, following agreements are captured in the Chairman’s note as
  A UE is configured with resources for PDSCH rate matching
    FFS details
  A UE is configured with resources for PUSCH rate matching
    FFS details

## Slide 3: Proposal
UE supports higher layer configuration of M RMR sets.
  RMR set may contain periodic RMR(s), where periodic RMR is configured with periodicity and slot offset (e.g. periodic ZP CSI-RS).
  RMR set may contain semi-persistent RMR(s), where semi-persistent RMR is configured with periodicity (FFS: slot offset) (e.g. semi-persistent ZP CSI-RS).
  RMR set may contain aperiodic RMR(s), where aperiodic RMR is configured without periodicity and slot offset (e.g. PDSCH starting symbol, aperiodic ZP CSI-RS).
    For aperiodic RMR, at least X’=0 is supported, where X’ is the slot offset from the slot where DCI signaled to the slot where actual RMR is applied.
  FFS: signaling details.
DCI is used to indicate one or more RMR set(s) from RMR sets for a given slot.
  FFS: The number of RMR sets indicated by DCI
  FFS detailed signaling (e.g. PQI-like signaling, explicit signaling)
FFS whether MAC CE can be used to activate N out of M RMR sets for DCI indication.
Note that the name of RMR is used for the convenience of discussion and can be revised if needed.
  As example, RMR may consist of REs indicated by CSI-RS configurations, and/or SRS configurations, or a bitmap.