## Slide 1: WF on defining frequency-granularities for CSI reporting and CSI-RS
Ericsson, LGE, Samsung , Intel, [Qualcomm, Docomo, Huawei],. …
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21st – 25th August, 2017
Agenda item 6.1.2.2.3
R1-1715045

## Slide 2: Previous Agreements
Agreements:
  Define “CSI reporting band” as a collection of (contiguous or non-contiguous) subbands pertinent to a CSI reporting setting
    FFS how the CSI reporting band is determined
  Three frequency granularities are supported:
    Wideband reporting
    Partial band reporting
    Subband reporting
  …
  Support at least following configurations of NR CSI-RS
    UE-specific configuration to support
      Wideband CSI-RS, i.e. from UE perspective, the full bandwidth the UE is configured to operate with
      Partial-band CSI-RS, i.e. from UE perspective, part of the bandwidth the UE is configured to operate with
      FFS: Different patterns may be used for wideband and subband CSI-RSs
  …
  For partial-band CSI-RS, partial-band can be the same as bandwidth part
    FFS whether or not to have small values than the bandwidth of bandwidth part

## Slide 3: Proposal
A subband is defined as N contiguous PRBs, the value of N depends on the bandwidth of the active bandwidth part
  FFS if value of N is fixed for a certain bandwidth or configurable from a set of values or if it depends on RBG /PRG size
A CSI-RS resource configuration includes the BWP information and the bandwidth of the CSI-RS is either
  “Wideband”: The UE shall assume the CSI-RS occupies the full bandwidth part
  “Partial band”: The UE shall assume the CSI-RS occupies a subset of contiguous subbands within the bandwidth part
    Note: A UE may be pre-configured with a partial band configuration for each candidate bandwidth part independently
FFS if a CSI report setting configuration defines a CSI reporting band as a subset of subbands of the bandwidth part or if the CSI reporting band always corresponds to the CSI-RS bandwidth
  The UE is not expected to be configured with a CSI reporting band which contains subbands where RSs for channel and interference are not present

## Slide 4: Example
Subband
CSI reporting band
2 Subbands
Partial band CSI-RS
Active bandwidth part
Carrier bandwidth