## Slide 1
WF on DL PRB Bundling
vivo, Huawei, Hisi, Qualcomm, Nokia, E///, [Samsung]
3GPP TSG RAN WG1 RAN1 NR Ad hoc #2
Prague, Czech, 21st – 25th May 2017
R1-171xxxx

## Slide 2: Background
Agreements:
For DL data transmission:
  PRB bundling size values include
    Case 1: one or more values down-selected from the following set
      {[1], 2, 4, 8 and 16};
      FFS the relationship with RBG size;
    Case 2: values equal to consecutively scheduled bandwidth in frequency;
  For UE-specific PRB bundling size indication, support dynamically indicated PRB bundling size with up to 1 bit overhead;
    FFS implicit indication to reduce configuration overhead, e.g., based on DMRS configuration etc;
    FFS the usage of above 1 bit, e.g. whether to switch between Case 1 and Case 2 or between two configured Case 1 values;
    FFS other aspects related to MU-MIMO pairing and higher-layer signaling

## Slide 3: Proposals
For DL data transmission:
  Case 1 PRB bundling size values are 2 and 4
The 1 DCI bit is flexibly used to switch between any configured values:
  The configured values could be two case 1 values;
  The configured values could be case 2 value and one case 1 value;
FFS: PRG configuration for broadcast PDSCH;
PRB bundle is based on absolute PRB-grid of a component carrier;