## Slide 1: WF on power sharing on MR-DC
AT&T, Bouygues Telecom, China Telecom, China Unicom, Deutsche Telekom, KT Cop. , NTT-Docomo, Orange, Telecom Italia, T-Mobile USA, Vodafone, Sprint,
R1-1715083
A.I. 6.1.7.1

## Slide 2: Current status of power sharing
Regarding power sharing for LTE-NR dual connectivity, support at least semi-static power sharing between LTE and NR
  FFS details
  Discuss further whether or not to support dynamic power sharing between LTE and NR
Discuss further impacts due to other factors, e.g., different TTI lengths, channel/service types, synchronous vs. asynchronous, different processing latency for LTE vs. NR, assumption regarding communication between NR vs. LTE at UE, specification impact to LTE (if any) and/or NR, etc.

## Slide 3: Deployment consideration
LTE coverage shall not be impacted due to the introduction of LTE-NR DC.
LTE uplink link budget depends on the maximum power available for uplink transmission. It is imperative that in deployment where DC is utilized that power sharing not be limited to cases that would negatively impact connectivity.

## Slide 4: Proposal
UE configured with LTE-NR dual-connectivity shall be able to transmit LTE using maximal power when NR transmission is not needed.
UE configured with LTE-NR dual-connectivity shall be able to transmit NR using maximal power when LTE transmission is not needed.
Regarding power sharing for LTE-NR dual connectivity, support dynamic power sharing between LTE and NR to maintain maximum allowable power for LTE and NR uplink.