## Slide 1: WF on CBG construction
Huawei, HiSilicon, OPPO, AT&T, Samsung
3GPP TSG RAN WG1 Meeting #90 R1-1715098
Prague, Czech Republic, 21 - 25 August 2017
Agenda item: 6.1.3.3.4.1

## Slide 2: Background
RAN1#89 Agreements:
For grouping CB(s) into CBG(s), following is adopted.
  With indicated number of CBGs, the number of CBs in a CBG changes according to TBS.
    FFS for the case of re-transmission or the case when the number of CBs is smaller than the indicated number of CBG
    FFS “indicated” is realized by RRC, MAC, L1 signalling
Following was approved by Email discussion [NRAH2-08]:
For the indicated number of CBGs per TB where “indicated” is realized by RRC, MAC, L1 signalling, the following options are considered for down-selection in RAN1#90.
  Option 1. RRC signaling (for bit-field size)
  Option 2. L1 signaling (for indication the number of CBGs per TB) + RRC signaling (for bit-field size)
  Option 3. both Option 1 and Option 2

## Slide 3: Proposal
At least for single CW case
  The maximum number N of CBG(s) per TB is configured by RRC signaling
    The number M of CBG(s) in the TB equals to min(C, N), where C is the number of CB(s) within the TB.
  For CBG construction
    The first Mod(C,M) CBG(s) out of total M CBG(s) include ceil(C/M) CB(s) per CBG
    The remaining M-Mod(C,M) CBG(s) include floor(C/M) CB(s) per CBG.