## Slide 1
3GPP TSG RAN WG1 Meeting #90 Prague, P.R. Czechia, 21st – 25th August 2017
Agenda: 6.1.2.2.3
WF on CSI Format Design
Samsung, Ericsson, NTT DOCOMO, Qualcomm, CATT, Nokia, NSB, Huawei, HiSilicon, ZTE, Interdigital, CHTTL, Verizon, BT, KDDI, CEWiT, IITH, Tejas Networks, IITM, Reliance Jio, Deutsche Telekom, AT&T, Vodafone, Sharp, Softbank, Fujitsu, Panasonic, LG Electronics, Mediatek
R1-1715288

## Slide 2: Background
Agreements:
  Periodic CSI reporting is carried at least on
    Short PUCCH
    Long PUCCH
  Type I CSI feedback is supported for P/SP/A-CSI and can be carried on either one of PUCCH and PUSCH
  Type I subband CSI can be carried on either one of PUSCH and long PUCCH
  Type II CSI is carried at least on PUSCH
    FFS CSI on PUCCH

## Slide 3: Encoding of CSI parameters for PUCCH-based reporting
For short PUCCH:
  Only single-slot reporting, no multiplexing of CSI parameters of a report in multiple slots
  Down select one of the following alternatives in RAN1 NR-AH3:
    Alt. 1: RI/CRI/PMI/CQI jointly encoded
    Alt. 1B: RI/CRI/PMI/CQI with padding bits prior to encoding (to ensure the same payload irrespective of RI)
For long PUCCH:
  Only single-slot reporting, no multiplexing of CSI parameters of a report in multiple slots
  Down select one of the following alternatives in RAN1 NR-AH3:
    Alt. 1: RI/CRI/PMI/CQI with padding bits prior to encoding (to ensure the same payload irrespective of RI)
      FFS if payload size depends on RI (or CRI, if present)
    Alt. 2: RI/CRI encoded separately from PMI/CQI
      Resource mapping/coding should consider payload size variation for different RI values

## Slide 4: Encoding of CSI parameters for PUSCH-based reporting
For Type I: only single-slot reporting
  A CSI report is composed of up to 2 parts
      Part 1: RI/CRI, CQI for the 1st CW
        FFS: if only wideband CQI is used for the first part
      Part 2: PMI, CQI for the 2nd CW (when RI>4)
For Type II:
  A CSI report is composed of up to 2 or 3 parts (to be down selected in RAN1 NR-AH3)
  If 3 parts are supported, part 1: RI, CQI for the 1st CW; part 2: wideband amplitude information; part 3: PMI
    FFS: if only wideband CQI is used for the first part
  If 2 parts are supported, details of parts are FFS
  Resource allocation for CSI reporting should take into account the payload difference between RI=1 and RI=2. Consider both single-slot and multi-slot reporting.
    Strive to maintain single-slot reporting principle (no multiplexing of CSI parameters of a report in multiple slots)
FFS: For codebook based on BF CSI-RS
FFS: Concurrent use of PUCCH and PUSCH reporting in different slots
FFS: RE mapping and layer mapping of UCI symbols
FFS: Reporting mechanism for the case where PUSCH and PUCCH collide in one slot

## Slide 5: CSI reporting characteristics
 | Periodic CSI (P-CSI) | Semi-persistent CSI (SP-CSI) | Aperiodic CSI (A-CSI)
Frequency granularity | Wideband or partial band(+) | Wideband, partial band, or subband | Wideband, partial band, or subband
Physical channel being used | Short PUCCH or long PUCCH (*) | Short PUCCH, long PUCCH, or PUSCH (*)(**) | PUSCH (****)
Codebook(s) | Type I CSI | Type I and II CSI (***) | Type I and II CSI
(+) FFS: if partial band is a portion of a bandwidth part; wideband is an entire bandwidth part
(*) FFS: The conditions for using short PUCCH vs. long PUCCH
To be concluded in RAN1 NR-AH3
(**) FFS: Potential down selection of the three options
(***) Type II CSI is only applicable for PUSCH (if supported)
FFS: support for partial Type II CSI reporting for SP-CSI
(****) If Y=0 supported, A-CSI can also be reported over short PUCCH, e.g. for WB CQI for URLLC