## Slide 1: WF on SL TX power control for FeD2D
LG Electronics, ZTE, Intel
3GPP TSG RAN WG1 Meeting #90 R1-1714736
Prague, Czech Republic, 21st – 25th Aug 2017
Agenda item: 5.2.9.2.3.3

## Slide 2: Background
In RAN1#89, the following agreements were made with regard to sidelink power control aspect for FeD2D:
  For sidelink power control for FeD2D, unless instructed by TPC command from the eNB, the UE transmits at a power no larger than the calculated power based on open loop power control between the UE and the eNB as described in Section 14.1.1.5 of TS 36.213
    Maximum power of sidelink transmission, and open loop power control parameters (P0, alpha) are configured by eNB.
    For out of coverage operation power control parameters (P0, alpha = 0) can be pre-configured
    FFS if UE is not required to monitor DL
  UE can set transmit power below the upper limit based on UE-UE channel propagation conditions
    FFS details and specification impact (e.g. whether the power setting can be up to UE implementation or mandated by specification)

## Slide 3: Proposals
  The exact SL TX power setting under the upper bound is up to UE implementation.
  e.g., UE-UE pathloss is taken into account in sidelink transmit power by UE implementation
  SL-RSRP is used to estimate sidelink pathloss.
  FFS whether SL-RSRP is based on DM-RS of discovery or another sidelink channel (e.g., PSSCH/PSCCH)
  FFS mechanism to know TX power level for sidelink pathloss measurement