## Slide 1: WF on UL/DL interlacing in TDD
LG Electronics, …
R1-1714775
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21th – 25th August 2017
Agenda item 5.2.7.6.3

## Slide 2: Background
In FDD, DL and UL transmissions will not be scheduled in parallel, i.e. if a DL transmission has been scheduled an UL transmission shall not be scheduled until HARQ RTT Timer of the DL HARQ process has expired (and vice versa).

## Slide 3: Background
In TDD,
  downlink and uplink subframe are placed in a staggered way every 5msec or 10msec.
  the number of consecutive downlink subframs between two discontinuous uplink subframes is not sufficient time for UE to save power consumption by turning off and on its power taking into account the practical amount of time for ramping down and up.

## Slide 4: Proposals
In TDD NB-IoT, DL and UL HARQ can be scheduled in parallel.
  UE can expect NPDCCH for PDSCH scheduling before completion of HARQ process for a PUSCH transmission.
  UE can expect NPDCCH for PUSCH scheduling before completion of HARQ process for a PDSCH reception.
  UE can receive a NPDSCH in DL subframes before completion of a NPUSCH transmission in UL subframes.
  UE can transmit a NPUSCH in UL subframes before completion of a NPDSCH reception in DL subframes.
  FFS on single DCI for both DL and UL scheduling or single DCI per DL or UL scheduling
In TDD NB-IoT, early termination of PDSCH and PUSCH is supported.
  UE can report ACK/NACK during a PDSCH reception
  eNB can terminate UE’s PUSCH transmission by NPDCCH

## Slide 5: Appendix
Completion of HARQ process for a PUSCH transmission
  represents the time interval from the ending subframe of PDCCH for the associated UL grant to the first subframe of the next NPDCCH monitoring search space.
Completion of HARQ process for a PDSCH transmission
  represents the time interval from “the ending subframe of PDCCH for the associated DL grant to the first subframe of the next NPDCCH monitoring search space.