## Slide 1: Way forward on remaining issues of single UL transmission
NTT DOCOMO, APPLE, LG Electronics
3GPP TSG RAN WG1 Meeting #90
Prague, Czech Republic, 21th – 25th August 2017
A.I. 6.1.6
R1-1714827

## Slide 2: Proposal
For UE with simultaneous UL transmissions on different carriers (where there is at least one LTE carrier and at least one NR carrier of a different carrier frequency), define UE capability of single UL transmission
  If UE is configured with single UL transmission, support the following
    UE is configured with DL-reference UL/DL configuration defined for FDD-SCell in TDD-FDD CA with TDD-PCell
      For scheduling/HARQ timing of LTE FDD carrier, DL-reference UL/DL configuration defined for FDD-SCell in TDD-FDD CA with TDD-PCell is applied
      UE is allowed to transmit NR UL signals in the subframe(s) where LTE UL transmission is not allowed according to the DL-reference UL/DL configuration
Send an LS to RAN2, RAN3, and RAN4