## Slide 1: WF on uplink operation with SUL for LTE-NR UL Coexistence
Huawei, HiSilicon, MediaTek, China Telecom
3GPP TSG RAN WG1 meeting #90 R1- 1714834
Prague, Czech Republic, 21 – 25 August, 2017
Agenda item: 6.1.6

## Slide 2: Background
Agreements:
Specify mechanisms for supporting supplementary Uplink frequency
  Note: SUL herein refers to the case when there is only UL resource for a carrier from NR perspective
  Use SUL as complimentary access link (including from random access point of view) to NR TDD and to NR FDD, where the UE may select PRACH resources either in the NR TDD/FDD uplink frequency or the SUL frequency.
  Note: The SUL frequency can be a frequency shared with LTE UL(at least for the case when NR spectrum is below 6 Ghz).
    Minimize impact to NR physical layer design to enable this co-existence
  Note: whether or not UE has to support simultaneous transmission on uplink frequencies is a separate discussion

## Slide 3: Background
Agreements:
For NR standalone operation for a UE,
  NR supports that the UE is allowed to transmit on UL carriers on different frequency ranges but the UE has the capability to only transmit on one of the carriers at a given time in the following case:
    case of SRS carrier switching with at least one of the frequency ranges agreed for LTE-NR UL sharing by RAN4 (e.g. refer to R4-1704411)

## Slide 4: Background
Agreements:
Support the following solution to single UL transmission where NW synchronization between eNodeB and gNodeB is assumed (where there is at least one LTE carrier and at least one NR carrier of a different carrier frequency)
  When UE is activated with multiple UL carriers on different frequencies, time-switching of LTE UL carrier and NR UL carrier is used
    UL transmission timing pattern of LTE carrier and NR carrier is semi-statically shared between eNodeB and gNodeB
    FFS: Signaling to UE of UL transmission timing pattern
  …..
  Other solutions are not precluded

## Slide 5: Proposal
For a UE capable to only transmit on one carrier at a time, NR supports for UE uplink operations with SUL
  Multiple patterns of reserved time resources (e.g. slots) can be configured to one UE for each configured UL carrier (including SUL carrier). Which pattern is active is informed to the UE via MAC CE.
    FFS the minimum activation timer for the uplink carrier.
    There is neither NR PUSCH nor NR PUCCH transmission within those reserved time resources.
    The reserved time resource in patterns can prevent UE from simultaneous UL transmission on both UL carriers and allow the switching moment of UL carriers to be known by UE in advance.
  Note: For a UE capable of multiple UL transmissions simultaneously, the UE may be allowed to transmit simultaneously on multiple UL carriers if there is no IMD issue.
Sent an LS accommodating above agreement to RAN2