## Slide 1: WF on Discovery Enhancements for Bandwidth Limited UEs
Intel, Sony, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #90 R1-1714844
Prague, Czech Republic, 21st – 25th August 2017
Agenda item - 5.2.9.2.2

## Slide 2: Background
Agreement at RAN1#89:
  The following discovery design enhancements are further studied
    Multi-shot discovery transmission across bandwidth of discovery pool(s) for Relay UE
    eNB assistance signaling to allow/improve Relay UE discovery
    Association of discovery transmission and reception resources
    Narrowband definition for discovery operation including 1 PRB and 6 PRB narrowband
  FFS whether discovery enhancements can be discovery model specific
  Other design options are not precluded

## Slide 3: Proposal
Sub-channelization of sidelink discovery pools is supported
For Model A discovery, multiple transmissions on different sub-channels are supported
  Note: this does not preclude possibility to define primary and secondary sub-channels for multiple transmissions
For Model B discovery, the following discovery enhancements are supported
  Sidelink discovery resource(s) for solicitation is/are associated with sidelink discovery resource(s) for response
    FFS whether association is predefined by specification or signaled by Relay UE
  Discovery response provided through eNB along with SD-RSRP information is supported