## Slide 1: WF on 64QAM support
Samsung, Ericsson…
3GPP TSG RAN WG1 Meeting #90 R1-1714958
Prague, Czechia 21th – 25th August 2017
Agenda item - 5.2.3.2

## Slide 2: Background
The following objective was included in 3GPP V2X Phase 2 WI description (RP-170798)
  Specify solutions for the following PC5 functionalities, which can co-exist in the same resource pools as Rel-14 functionality and use the same scheduling assignment format (which can be decoded by Rel-14 UEs), without causing significant degradation to Rel-14 PC5 operation compared to that of Rel-14 UEs: [RAN1, RAN2, RAN4]
    Carrier aggregation (up to 8 PC5 carriers);
    64QAM;
    Reduce the maximum time between packet arrival at Layer 1 and resource selected for transmission;
    Radio resource pool sharing between UEs using mode 3 and UEs using mode 4;

## Slide 3: Proposals
One bit from the reserved bits is used to differentiate Rel-15 transmission and Rel-14 transmission
5-bit MCS field in existing SCI-1 is used to indicate 64QAM.
For Imcs > 20 (64QAM), a scaling factor is applied on the number of scheduled PRBs for TBS determination, similar to DwPTS and partial end subframe in LAA
  FFS value of scaling factor
FFS: Study less PSD boosting for PSCCH, when PSSCH is 64QAM.
Study on new requirement of maximum PSSCH TBS and soft buffer handling.

## Slide 4: Illustration on spectrum efficiency