## Slide 1: Way Forward for NR RLM Thresholds
CATT, […]
3GPP TSG RAN WG1#90 R1-1714962
Prague, Czech Republic, 21st – 25th August 2017
Agenda 6.1.1.5.3

## Slide 2: Background
Agreements (RAN1#89)
  IS and OOS indications are based on SINR-like metric (e.g., hypothetical PDCCH BLER) as in LTE
    SINR-like metric as in LTE represents whether or not UE can receive PDCCH
    FFS: PDCCH in U-SS and/or PDCCH in C-SS
  RS used to derive SINR-like metric is down selected from following options
    Opt.1: CSI-RS
    Opt.2: DMRS for NR-PDCCH in C-SS
    Opt.3: DMRS for NR-PBCH
    Opt.4: NR-SSS
    Opt.5: RS for time/frequency tracking (if separate RS from above is defined for time/frequency tracking)
    FFS: how many options are used
  RAN1 assumes that single IS or OOS is indicated per reporting instance regardless number of beams available in cell. RAN1 has not concluded whether IS/OOS indications for RLF are per cell or not.
  RAN1 plans to provide at least periodic IS/OOS indications.
    FFS: possibility of additional aperiodic IS indication e.g., based on beam failure recovery mechanism.

## Slide 3: Background (cont.)
Agreements (RAN1 AH#2):
  The RS used for RLM should have following properties
    Periodic transmission with short enough periodicity
    Wideband transmission relative to bandwidth of active bandwidth part
    Supporting both single beam and multi-beam operations
    Representing control channel quality
  Both CSI-RS based RLM and SS block based RLM are supported
    FFS: whether or not only a single type of RS is configured to UE for RLM at a time

## Slide 4: Background
    Regardless which SINR-like metric (e.g., hypothetical PDCCH BLER) is adopted in RAN1, if similar approach as LTE is used, the UE will define internally the RLM out-of-sync and in-sync thresholds corresponding to the adopted SINR-like metric, and decide its out-of-sync and in-sync status based on the comparison of the RLM measurements based CSI-RS and/or SS-block SS and the internal RLM out-of-sync and in-sync thresholds.
    In current LTE RLM approach the network has no control on RLM out-of-sync and in-sync thresholds. Thus, it lacks the flexibility when a UE is required to support different coverage levels under different scenarios (e.g., mMTC UEs may be configured to support different coverage enhancement levels).
    For NR the exact values of Qin and Qout are not yet discussed/decided. Different type of services could tolerate higher or lower error rate on PDCCH, and thereby could benefit from being able to configure the applied thresholds for IS/OOS indications.

## Slide 5: Proposal
NR supports configurable in-sync threshold and out-of-sync thresholds for a UE
  The following options can be considered
  Option 1: the network may adjust the Qin and Qout thresholds with a restricted set of adjustment values
    FFS: the set of values for the adjustment.
  Option 2: the network configures the Qin and Qout thresholds for a UE among a restricted set of Qin/Qout thresholds.
    FFS: the set of values of Qin/Qout thresholds
  Option 3: the network configures the BLERs for hypothetical PDCCH among a restricted set of BLER values for Qin/Qout thresholds
    FFS: the set of values of BLERs for the configuration
  Other option is not precluded