## Slide 1: Way forward on PT-RS antenna port association
Intel, Huawei, HiSilicon, Ericsson, Samsung, Docomo, Spreadtrum, CMCC ...
3GPP TSG RAN WG1 Meeting #90 R1-1714977
Prague, Czechia, 21st – 25th August 2017
Agenda Item: 6.1.2.3.4

## Slide 2: Background
Agreements in RAN1 NR AH #2:
  If one DL PT-RS port is configured for a DL DM-RS port group, the DL PT-RS port and one DL DM-RS port in the DL DM-RS port group are associated for phase tracking, the association is determined in the specification
      FFS details for the association
  If one DL PT-RS port is configured for a DL DM-RS port group, the DL PT-RS port is associated with:
    Alt 1: the lowest DL DM-RS port in the DL DM-RS port group.
    Alt 2: one DL DM-RS port in the DL DM-RS port group in a RB, where the one DL DM-RS port may vary across RBs
    Other alternatives are not precluded
    To conclude with one alternative next meeting
  FFS the case of two codewords
  Study further whether or not to support power boosting for PT-RS considering different or same number of ports compared with DM-RS

## Slide 3: Proposal
  For UL, At least for codebook based transmission, if one PT-RS port is configured for an DM-RS port group, the PT-RS port is associated with a configured DM-RS port in the DM-RS port group.
    FFS: Such signalling is carried by RRC or MAC-CE or DCI
    FFS: non-codebook based case
  For DL, if one PT-RS port is configured for an DM-RS port group,
    For 1 CW case, the PT-RS port is associated with the lowest DM-RS port.
    For 2 CW case, the PT-RS port is associated with the lowest DM-RS port of the DM-RS ports for the higher MCS CW.
      If MCS of the 2 CWs is the same, CW 0 is selected
    UE can provide some information to facilitate gNB to map the PT-RS port onto the layer with higher received SINR.
      FFS: information details, e.g. signaling carried by MAC-CE or UCI, UL signal e.g. SRS
  For SU-MIMO, support power boosting for PT-RS
    FFS: spec impact