## Slide 1: WF on Q_in and Q_out thresholds for radio link monitoring
NTT DOCOMO, Ericsson, AT&T, [CATT], […]
3GPP TSG RAN WG1 Meeting #90 R1-1715213
Prague, Czech Republic,
21th – 25th August 2017
Agenda item: 6.1.1.5.3
Document for decision

## Slide 2: Background
R1-1714670 WF on configuration of RS used for radio link monitoring NTT DOCOMO
Agreements:
NR supports RLM on PCell and PSCell only
For RLM, NR supports to configure a single type of RS for a CORESET for a UE at a time
  FFS on interference measurement resource for each RS type
Signal and interference measurements for a given CORESET may be performed by using same RX beam
Continue offline discussion until Tuesday – Hiroki (DOCOMO)
FFS whether NR defines Q_in and Q_out thresholds per CORESET
FFS whether different RS types can be configured to different CORESETs for RLM

## Slide 3: Background
R1-1714962 WF on RLM threshold CATT
Possible agreements:
NR supports configurable Q_in/Q_out thresholds per UE
  A UE is configured with single Q_in threshold and single Q_out threshold
  Option 1: the network to make adjustment of the RLM out-of-sync and in-sync thresholds for a UE through UE-specific signaling
  Option 2: the network to make adjustment of the BLERs of PDCCH corresponding to the the out-of-sync and in-sync thresholds for a UE through UE-specific signaling
  Option 3: the network to select among restricted sets of Qin/Qout thresholds for a UE through UE-specific signaling
  Other option is not precluded

## Slide 4: Discussion
Alt.1: Single Q_in threshold and single Q_out threshold per CORESET are configured to UE
Alt.2: Single Q_in threshold and single Q_out threshold per UE are configured to UE
Alt.3: Single Q_in threshold and single Q_out threshold per CORESET are derived from specification
  e.g., based on service type associated with the CORESET
Alt.4: Single Q_in threshold and single Q_out threshold per UE are derived from specification
  e.g., based on UE type or only single Q_in and single Q_out are specified
…

## Slide 5: Proposal
NR supports configurable Q_in/Q_out thresholds for RLM
  Single Q_in and single Q_out are configured
    Alt.1: per CORESET
    Alt.2: per UE
    Alt.3: per RLM-RS
    Alt.4: per service type (e.g., eMBB, URLLC, …)
    Alt.5: per hypothetical PDCCH
  Specification defines candidate Q_in and Q_out values that should not be so many