## Slide 1: Way forward on scheduling request support in NR
Ericsson, NTT DOCOMO, Nokia, Nokia Shanghai Bell, Samsung, Panasonic
R1-1715218
RAN1 #90
Prague, Czech Republic, 21-25 August 2017
Ag. 6.1.3.3.2

## Slide 2: Background
To complete the NR design it is essential to define the signaling for SR operation.
Relevant RAN2 agreements (from LS R1-1710211)
  “Agreements
    Multiple SR configurations can be configured to the UE and which SR configuration is used depends on the LCH that triggers the SR. The granularity of SR configuration for a logical channel is FFS.
    From RAN2 point of view a single bit SR with multiple SR configuration is sufficient to distinguish the “numerology/TTI length” of the logical channel that trigger the SR. RAN2 has not identified other use cases for which multibit SR is need with sufficient support.
    RAN2 does not see the need to convey buffer status information.
    Send LS to RAN1 to indicate to RAN1 that RAN2 doesn’t see the need to support multi-bit SR. “

## Slide 3: Proposal
The UE can be configured with up to [4] separate SR configurations.
In case of SR only, the physical layer can only transmit one SR at any given time
  If multiple SR are triggered prioritization of which SR should be transmitted is decided by RAN2
Multiplexing of SR and HARQ feedback is supported on PUCCH
An SR can be configured with a periodicity of one OFDM symbol up to the largest periodicity supported in LTE (i.e. 80 ms)
  FFS: Supported periodicity values
One SR configured can be associated with either short or long PUCCH (of different lengths)