## Slide 1: WF on beam recovery request transmission
LG Electronics, Samsung, OPPO, Nokia, Nokia Shanghai Bell, InterDigital, AT&T, [Ericsson]
R1-1715225
3GPP TSG RAN1 meeting #90
Prague, Czech Republic, 21th – 25th Aug. 2017
Agenda Item: 6.1.2.2.7

## Slide 2: Background
Working assumption:
  Support at least the following triggering condition(s) for beam failure recovery request transmission:
    Condition 1: when beam failure is detected and candidate beam is identified at least for the case when only CSI-RS is used for new candidate beam identification
    FFS Condition 2: Beam failure is detected alone at least for the case of no reciprocity
      FFS how the recovery request is transmitted without knowledge of candidate beam
    Note: if both conditions are supported, which triggering condition to use by UE also depends on both gNB configuration and UE capability
Support the following channel(s) for beam failure recovery request transmission:
  Non-contention based channel based on PRACH, which uses a resource orthogonal to resources of other PRACH transmissions, at least for the FDM case
  Support using PUCCH for beam failure recovery request transmission
Beam failure is declared only when all serving control channels fail.
When a subset of serving control channels fail, this event should also be handled
  Details FFS

## Slide 3: Proposals
When beam failure is declared and at least one new candidate beam is identified, non-contention based channel based on PRACH is used for beam recovery request transmission.
When a subset of serving control channels fails, PUCCH channel(s) is used for beam switching request transmission.