## Slide 1: WF on DMRS port mapping table
Panasonic, ….
R1-1715231
3GPP TSG RAN WG1 Meeting RAN1 #90
Prague, Czech Republic 21st – 25th August 2017
Agenda item: 6.1.2.3.3

## Slide 2: Background
Agreements (RAN1 NR AH2) :R1-1711784
A UE is configured by higher layers with DMRS pattern either from the front-loaded DMRS Configuration type 1 or from the front-loaded DMRS Configuration type 2 for DL/UL:
  Configuration type 1:
    One symbol:
      Comb 2 + 2 CS, up to 4 ports
    Two symbols:
      Comb 2 + 2 CS + TD-OCC ({1 1} and {1 -1}), up to 8 ports
        Note: It should be possible to schedule up to 4 ports without using both {1,1} and {1,-1}.
  Configuration type 2:
    One symbol:
      2-FD-OCC across adjacent REs in the frequency domain, up to 6 ports
    Two symbols:
        2-FD-OCC across adjacent REs in the frequency domain + TD-OCC (both {1,1} and {1,-1}) up to 12 ports
          Note: It should be possible to schedule up to 6 ports without using both {1,1} and {1,-1}.
  From UE perspective, frequency domain CDMed DMRS ports are QCLed.
  FFS: Whether the front-load DMRS configuration type for a UE for UL and DL can be different or not.
  Note: If there are significant complexity/performance issues involved in the above agreements, down-selection can still be discussed
Agreements (RAN1 NR AH2) :R1-1711771
The number of front-load DMRS symbols can be 1 or 2 when the number of DMRS ports allocated to UE is equal or less than N
  N is 4 for Configuration 1 and 6 for Configuration 2.
  FFS the details to determine 1 or 2 symbols

## Slide 3: Motivation
Reduce the DMRS port mapping table to reduce the DCI signaling overhead by applying a defined set of principles
Provide better support for indication of MU-MIMO

## Slide 4: Proposals
NR should apply following set of principles together to generate DMRS port mapping table shown in next slides
  Allow mapping to port index in a consecutive manner
    Example. User 1 has 2 layers. Then user 1 is mapped to p1 and p2 or p2 and p3 and so on, but not on p1 and p3 or p1 and p4 and so on.
  Users with higher number of layers are mapped first to lower port index
    Example: User 1 has 3 layers, user 2 has 2 layers, user 3 has 4 layers. Then user 3 is mapped first to p1-p4, followed by user 1 to p5-p7 and user 2 to p8-p9
    Note: This doesn’t have any restriction on the scheduling decision
  Users with more than one layer should be mapped to the ports within the same CDM group, whenever the number of layers is less than or equal to CDM group size
  For a given user with more than one layer, two indexes should be assigned to the same layer-to-port mapping combination for indicating the SU-MIMO or MU-MIMO
  Support codeword enabling to indicate the presence of more than 4 layers/UE in SU-MIMO (similar to LTE)
Single DCI table should be supported for both 1-symbol and 2-symbol DMRS for each DMRS configurations type

## Slide 5: Proposal: DMRS port mapping table for DMRS configuration type 1
 |  |  |  |  | DMRS Configuration Type 1 |  |  |  |  | 
 | Codeword 0 enabled |  |  |  |  |  | Codeword 0 enabled |  |  | 
 | Codeword 1 disabled |  |  |  |  |  | Codeword 1 enabled |  |  | 
Index | Number of layers/UE | Ports | Nr. of symbols | MU/SU-MIMO |  | Index | Number of layers/UE | Ports | Nr. of symbols | MU/SU-MIMO
0 | 1 | p1 | 1-symbol |  |  | 0 | 5 | p1-p5 | 2-symbol | 
1 | 1 | p2 | 1-symbol |  |  | 1 | 6 | p1-p6 | 2-symbol | 
2 | 1 | p3 | 1-symbol |  |  | 2 | 7 | p1-p7 | 2-symbol | 
3 | 1 | p4 | 1-symbol |  |  | 3 | 8 | p1-p8 | 2-symbol | 
4 | 2 | p1-p2 | 1-symbol |  |  | 4 | - | reserved |  | 
5 | 2 | p3-p4 | 1-symbol |  |  | 5 | - | reserved |  | 
6 | 3 | p1-p3 | 1-symbol |  |  | 6 | - | reserved |  | 
7 | 4 | p1-p4 | 1-symbol |  |  | 7 | - | reserved |  | 
8 | 1 | p1 | 2-symbol |  |  | 8 | - | reserved |  | 
9 | 1 | p2 | 2-symbol |  |  | 9 | - | reserved |  | 
10 | 1 | p3 | 2-symbol |  |  | 10 | - | reserved |  | 
11 | 1 | p4 | 2-symbol |  |  | 11 | - | reserved |  | 
12 | 1 | p5 | 2-symbol |  |  | 12 | - | reserved |  | 
13 | 1 | p6 | 2-symbol |  |  | 13 | - | reserved |  | 
14 | 1 | p7 | 2-symbol |  |  | 14 | - | reserved |  | 
15 | 1 | p8 | 2-symbol |  |  | 15 | - | reserved |  | 
16 | 2 | p1-p2 | 2-symbol |  |  | 16 | - | reserved |  | 
17 | 2 | p1-p2 | 2-symbol | MU-MIMO |  | 17 | - | reserved |  | 
18 | 2 | p3-p4 | 2-symbol |  |  | 18 | - | reserved |  | 
19 | 2 | p3-p4 | 2-symbol | MU-MIMO |  | 19 | - | reserved |  | 
20 | 2 | p5-p6 | 2-symbol |  |  | 20 | - | reserved |  | 
21 | 2 | p5-p6 | 2-symbol | MU-MIMO |  | 21 | - | reserved |  | 
22 | 2 | p6-p7 | 2-symbol |  |  | 22 | - | reserved |  | 
23 | 2 | p6-p7 | 2-symbol | MU-MIMO |  | 23 | - | reserved |  | 
24 | 2 | p7-p8 | 2-symbol |  |  | 24 | - | reserved |  | 
25 | 2 | p7-p8 | 2-symbol | MU-MIMO |  | 25 | - | reserved |  | 
26 | 3 | p1-p3 | 2-symbol |  |  | 26 | - | reserved |  | 
27 | 3 | p1-p3 | 2-symbol | MU-MIMO |  | 27 | - | reserved |  | 
28 | 3 | p5-p7 | 2-symbol |  |  | 28 | - | reserved |  | 
29 | 3 | p5-p7 | 2-symbol | MU-MIMO |  | 29 | - | reserved |  | 
30 | 4 | p1-p4 | 2-symbol |  |  | 30 | - | reserved |  | 
31 | 4 | p5-p8 | 2-symbol |  |  | 31 | - | reserved |  | 

## Slide 6: Proposal: DMRS port mapping table for DMRS configuration type 2 (one codeword enabled)
 |  |  |  |  | DMRS Configuration Type 2 |  |  |  |  | 
 |  |  |  |  | Codeword 0 enabled |  |  |  |  | 
 |  |  |  |  | Codeword 1 disabled |  |  |  |  | 
Index | Number of layers/UE | Ports | Nr. of symbols | MU/SU-MIMO |  | Index | Number of layers/UE | Ports | Nr. of symbols | MU/SU-MIMO
0 | 1 | p1 | 1-symbol |  |  | 27 | 2 | p1-p2 | 2-symbol | MU-MIMO
1 | 1 | p2 | 1-symbol |  |  | 28 | 2 | p3-p4 | 2-symbol | 
2 | 1 | p3 | 1-symbol |  |  | 29 | 2 | p3-p4 | 2-symbol | MU-MIMO
3 | 1 | p4 | 1-symbol |  |  | 30 | 2 | p5-p6 | 2-symbol | 
4 | 1 | p5 | 1-symbol |  |  | 31 | 2 | p5-p6 | 2-symbol | MU-MIMO
5 | 1 | p6 | 1-symbol |  |  | 32 | 2 | p6-p7 | 2-symbol | 
6 | 2 | p1-p2 | 1-symbol |  |  | 33 | 2 | p6-p7 | 2-symbol | MU-MIMO
7 | 2 | p3-p4 | 1-symbol |  |  | 34 | 2 | p7-p8 | 2-symbol | 
8 | 2 | p5-p6 | 1-symbol |  |  | 35 | 2 | p7-p8 | 2-symbol | MU-MIMO
9 | 3 | p1-p3 | 1-symbol |  |  | 36 | 2 | p9-p10 | 2-symbol | 
10 | 3 | p1-p3 | 1-symbol | MU-MIMO |  | 37 | 2 | p9-p10 | 2-symbol | MU-MIMO
11 | 3 | p4-p6 | 1-symbol |  |  | 38 | 2 | p10-p11 | 2-symbol | 
12 | 3 | p4-p6 | 1-symbol | MU-MIMO |  | 39 | 2 | p10-p11 | 2-symbol | MU-MIMO
13 | 4 | p1-p4 | 1-symbol |  |  | 40 | 2 | p11-p12 | 2-symbol | 
14 | 1 | p1 | 2-symbol |  |  | 41 | 2 | p11-p12 | 2-symbol | MU-MIMO
15 | 1 | p2 | 2-symbol |  |  | 42 | 3 | p1-p3 | 2-symbol | 
16 | 1 | p3 | 2-symbol |  |  | 43 | 3 | p1-p3 | 2-symbol | MU-MIMO
17 | 1 | p4 | 2-symbol |  |  | 44 | 3 | p5-p7 | 2-symbol | 
18 | 1 | p5 | 2-symbol |  |  | 45 | 3 | p5-p7 | 2-symbol | MU-MIMO
19 | 1 | p6 | 2-symbol |  |  | 46 | 3 | p9-p11 | 2-symbol | 
20 | 1 | p7 | 2-symbol |  |  | 47 | 3 | p9-p11 | 2-symbol | MU-MIMO
21 | 1 | p8 | 2-symbol |  |  | 48 | 3 | p10-p12 | 2-symbol | 
22 | 1 | p9 | 2-symbol |  |  | 49 | 3 | p10-p12 | 2-symbol | MU-MIMO
23 | 1 | p10 | 2-symbol |  |  | 50 | 4 | p1-p4 | 2-symbol | 
24 | 1 | p11 | 2-symbol |  |  | 51 | 4 | p5-p8 | 2-symbol | 
25 | 1 | p12 | 2-symbol |  |  | 52 | 4 | p9-p12 | 2-symbol | 

## Slide 7: Proposal: DMRS port mapping table for DMRS configuration type 2 (two codewords enabled)
 |  |  |  |  | DMRS Configuration Type 2 |  |  |  |  | 
 |  |  |  |  | Codeword 0 enabled |  |  |  |  | 
 |  |  |  |  | Codeword 1 enabled |  |  |  |  | 
Index | Number of layers/UE | Ports | Nr. of symbols | MU/SU-MIMO |  | Index | Number of layers/UE | Ports | Nr. of symbols | MU/SU-MIMO
0 | 5 | p1-p5 | 1-symbol |  |  | 27 | - | reserved |  | 
1 | 6 | p1-p6 | 1-symbol |  |  | 28 | - | reserved |  | 
2 | 5 | p1-p5 | 2-symbol |  |  | 29 | - | reserved |  | 
3 | 6 | p1-p6 | 2-symbol |  |  | 30 | - | reserved |  | 
4 | 7 | p1-p7 | 2-symbol |  |  | 31 | - | reserved |  | 
5 | 8 | p1-p8 | 2-symbol |  |  | 32 | - | reserved |  | 
6 | - | reserved |  |  |  | 33 | - | reserved |  | 
7 | - | reserved |  |  |  | 34 | - | reserved |  | 
8 | - | reserved |  |  |  | 35 | - | reserved |  | 
9 | - | reserved |  |  |  | 36 | - | reserved |  | 
10 | - | reserved |  |  |  | 37 | - | reserved |  | 
11 | - | reserved |  |  |  | 38 | - | reserved |  | 
12 | - | reserved |  |  |  | 39 | - | reserved |  | 
13 | - | reserved |  |  |  | 40 | - | reserved |  | 
14 | - | reserved |  |  |  | 41 | - | reserved |  | 
15 | - | reserved |  |  |  | 42 | - | reserved |  | 
16 | - | reserved |  |  |  | 43 | - | reserved |  | 
17 | - | reserved |  |  |  | 44 | - | reserved |  | 
18 | - | reserved |  |  |  | 45 | - | reserved |  | 
19 | - | reserved |  |  |  | 46 | - | reserved |  | 
20 | - | reserved |  |  |  | 47 | - | reserved |  | 
21 | - | reserved |  |  |  | 48 | - | reserved |  | 
22 | - | reserved |  |  |  | 49 | - | reserved |  | 
23 | - | reserved |  |  |  | 50 | - | reserved |  | 
24 | - | reserved |  |  |  | 51 | - | reserved |  | 
25 | - | reserved |  |  |  | 52 | - | reserved |  | 
26 | - | reserved |  |  |  |  |  |  |  |