## Slide 1: WF on Sub-PRB for eFeMTC
Sierra Wireless, Ericsson, Nokia, NSB, KT Corp, Sony, AT&T, Verizon, Qualcomm …
3GPP TSG RAN WG1 Meeting #90bis R1-1718921
Prague, Czech Republic, Oct9th – 14th 2017
Agenda 6.2.5.6 UL Spectral Efficiency

## Slide 2: Proposal:
WA: Sub-PRB shall be supported in both CE Mode A and B
For Sub-PRB, the maximum total sub-frames of transmission shall not exceed:
    [32] sub-frames for CE Mode A
    [2048] sub-frames for CE Mode B
  FFS: Supported transport block sizes and number of repeats for each CE Mode
Sub-PRB shall increase resource unit (RU) length following the NB-IoT design
  E.g. 6 Tones RU=2 SF, 3 Tones RU=4 SF
  FFS: if more than one RU is allocated per transport block
For Sub-PRB, increasing DMRS shall not be supported
The Sub-PRB feature is configured/enabled by RRC signaling
The Sub-PRB resource allocation shall be signaled by DCI