## Slide 1
3GPP TSG RAN WG1 Meeting NR 90bis R1-1718982
Prague, Czech, Oct. 09-13 2017
Agenda item: 7.2.2.4
Way Forward on Candidate Beam Identification for Beam Failure Recovery
Huawei, HiSilicon, LGE, Intel, Interdigital
AT&T, vivo, Spreadtrum, Lenovo, Motorola Mobility Sharp, KT Corporation, OPPO, ZTE, SaneChips
Nokia, Nokia Shanghai Bell, China Telecom

## Slide 2: Agreement R1-1716920
For new candidate beam identification purpose
  In CSI-RS only case, a direct association is configured between only CSI-RS resources and dedicated PRACH resources
  In SS block only case, a direct association is configured between only SS block resources and dedicated PRACH resources
  In CSI-RS + SS block case (if supported), an association is configured between resources of CSI-RS/SSB and dedicated PRACH resources
    CSI-RS and SSB can be associated with the same dedicated resource through QCL association

## Slide 3: Proposal
Specification supports the CSI-RS + SS block case for the purpose of new candidate beam identification
  The above case is configured by gNB
  Note: a dedicated PRACH resource is configured to either an SSB or a CSI-RS resource
  Following two scenarios are supported when a UE is configured with CSI-RS + SSB
    Scenario 1: PRACHs are associated to SSBs only
      In this scenario, CSI-RS resources for new beam identification can be found from the QCL association to SSB(s).
    Scenario 2: Each of the multiple PRACHs is associated to either an SSB or a CSI-RS resource
  FFS: multiple SSB can be associated with the same uplink resource.