## Slide 1: WF on Subband Size for CSI
Samsung
3GPP TSG-RAN WG1#90bis R1-1718892
Prague, Czech Republic, 9th – 13rd October 2017
Agenda: 7.2.2.2

## Slide 2: Background
The following was agreed in RAN1 NR AH3 and #90bis:
  For CSI reporting, a subband is defined as N contiguous PRBs, the value of N depends on the bandwidth of the active bandwidth part
    FFS if value of N is fixed for a certain bandwidth or configurable from a set of values or if it depends on RBG /PRG size
For a given bandwidth of the active bandwidth part, a UE can be configured with one out of two subband sizes via higher layer signaling
Two values of PRG size: 2 and 4 PRBs
Carrier bandwidth part (PRBs) | Subband Size (PRBs)
24 – 60 | [6], [12]
61 – 100 | 8, [16]
101 – 150 | [10], [20]
151 – 200 | 12, [24]
201 – 275 | 16, [32]

## Slide 3: Proposal
  The agreed table is refined as follows (to align subband size with PRG size):
  The 2nd subband size values in brackets are to be confirmed or refined in RAN1#91
    Each of these 2nd values is an integer multiple of the corresponding 1st value
Carrier bandwidth part (PRBs) | Subband Size (PRBs): 1st value, 2nd value
24 – 60 | 8, [16]
61 – 100 | 8, [16]
101 – 150 | 12, [24]
151 – 200 | 12, [24]
201 – 275 | 16, [32]