## Slide 1: Proposals for frequency hopping (FH) for PUSCH
NTT DOCOMO, …
R1-1719201
3GPP TSG RAN WG1 Meeting #90bis
Prague, Czech Republic
9th - 13th October 2017
Agenda item: 7.3.3.4

## Slide 2: Background
Agreements: For DFT-s-OFDM based NR-PUSCH transmission, contiguous RB allocation with/without frequency hopping are supported At least intra-slot frequency hopping is supported for 14 symbol slot case FFS on detailed resource allocation FFS on detailed frequency hopping for PUSCH RP-172108 Updated work plan of RAN 1 and 4 NR UL resource allocations Aiming December 2017 completion: Specify the requirements for DFTS OFDM and CP-OFDM for PUSCH Aiming June 2018 completion: Relaxed resource allocations including non-contiguous allocation for PUSCH Agreements: For long PUCCH over multiple slots, inter-slot hopping is supported by configuration FFS details For long PUCCH over multiple slots, the intra-slot hopping and inter-slot hopping are not enabled at the same time for a UE

## Slide 3: Proposal (1)
Frequency hopping is supported for CP-OFDM based NR-PUSCH transmission with contiguous RB allocation
  At least intra-slot frequency hopping is supported for 14 symbol slot case
For UL transmission with grant, intra-slot FH hopping can be enabled/disabled by UL grant.

## Slide 4: Proposal (2)
For PUSCH with grant, at least following are supported and configured by RMSI or OSI:
  Inter-slot FH without intra-slot FH.
  Inter-slot FH + intra-slot FH.