## Slide 1: WF on Synchronization for carrier aggregation in eV2X
CATT, …
3GPP TSG RAN WG1 Meeting #90bis R1-1718891
Prague, Czechia, 9th – 13th August 2017
Agenda item - 6.2.3.1.2

## Slide 2: Background
In 3GPP V2X phase 2 WID (RP-170798), the following objectives for carrier aggregation operation is as follows:
  Specify solutions for the following PC5 functionalities, which can co-exist in the same resource pools as Rel-14 functionality and use the same scheduling assignment format (which can be decoded by Rel-14 UEs), without causing significant degradation to Rel-14 PC5 operation compared to that of Rel-14 UEs: [RAN1, RAN2, RAN4]
    Carrier aggregation (up to 8 PC5 carriers);

## Slide 3: Background (2)
Figure 1. The synchronization scenario for component carriers with timing alignment
Figure 2: The synchronization scenario for component carriers with timing offset

## Slide 4: Proposals
For Rel-15 CA, UE should select the highest priority synchronization source among group of sidelink CCs as the its synchronization reference for all the sidelink CCs in the group.
  For example, Rel-14 mechanism could be extended to multiple carriers within the group.