## Slide 1: Way forward on NPRACH power control
Huawei, HiSilicon, Ericsson, Softbank, Deutsche Telekom, China Telecom, China Unicom, Vodafone
R1-1718954
3GPP TSG RAN WG1 Meeting #90bis
Prague, Czech Republic, 9 – 13 October 2017
Agenda item 6.1.6

## Slide 2: Background
At RAN1#89 it was identified that the NB-IoT NPRACH power control mechanism may lead to high uplink interference and blocking at the eNB receiver in some scenarios [1].
At RAN1#90bis, different companies discuss and propose solutions [2][3][4].
[1] R1-1709672, “On uplink power control for Rel-13 NB-IoT”, Huawei , HiSilicon, RAN1#89, May 2017.
[2] R1-1716984, “On Rel-14 NB-IoT RACH power control”, Huawei , HiSilicon, RAN1#90bis, Oct 2017.
[3] R1-1717028, “On improved Random Access Procedure for NB-IoT Rel-14”, Ericsson, RAN1#90bis, Oct 2017.
[4] R1-1717192, “NPRACH power control for Rel-14 NB-IoT”, ZTE, SaneChips, RAN1#90bis, Oct 2017.

## Slide 3: Proposals
Agree to introduce the following solutions for Rel-14 to reduce the possible uplink interference caused by the NB-IoT UE which has level ramped from NPRACH level 0 in a RACH procedure.
  For a Rel-14 UE which has level ramped from NPRACH level 0 in a RACH procedure, use the NPRACH level 0 power control and power ramping procedure in the new NPRACH level, i.e. based on path-loss with power ramping.
  Network can configure a cell-specific Δ additional to the NRSRP threshold of CE level 0 to indicate that the UE shall not perform level ramping when it measures NRSRP higher than “NRSRP threshold of CE level 0 + Δ”, Δ from the set {0, 10, 20, 30} dB.
    The UE above which does not perform level ramping shall consider the Random Access procedure unsuccessfully completed when it fails at the maximum number of attempts (i.e. maxNumPreambleAttemptCE) configured in CE level 0.
  For a Rel-14 UE which has level ramped from NPRACH level 0 in a RACH procedure, network can configure whether NPUSCH power control for Msg3 shall be according to the existing open loop power control functionality in TS 36.213 but without the restriction on the number of repetitions.
Prepare CR to TS36.213 and send LS to inform RAN2 accordingly.