## Slide 1: WF on antenna group signaling
MediaTek, Nokia, NSB, Intel, …
3GPP TSG RAN WG1 #90 bis R1-1718962
Prague, Czech, October 9th-13th 2017
Agenda item: 7.1.2.1.2

## Slide 2: Background
At RAN1 #90, the following was agreed:
  Specify UE capability identifying if UL MIMO capable UE can support coherent transmission across its transmit chains
    FFS: if UE capability identifies if coherent transmission is supported on all of, vs. none of, vs. on a subset, of its transmit chains
    FFS: how UL MIMO precoding design takes into account the above capability
Notes: Agreements:
For cross link interference mitigation,
  Further consider UE-UE measurement and reporting, and TRP-TRP measurement
    Details FFS, including at least the RS for measurement, the metric for measurement (e.g., RSRP), long-term vs. short-term, etc., especially considering consistency with other NR topics
    Aim in RAN1#89 to come up with detailed option(s) including potential down-selecting from the list concluded from the SI
    Once the detailed option(s) is available, decide whether or to support this feature
  For the case of TRP-TRP measurement, study whether or not there is additional RAN1 specification impact
  Further consider other aspects, e.g., power control, sensing, timing related handling, etc.

## Slide 3: Proposal
A UE can signal to the gNB one or multiple transmit chain groups:
  Within each transmit chain group, coherent transmissions from different transmit Chains are supported by the UE;
  Coherent transmissions from transmit chains from different transmit chain groups are not guaranteed by the UE.