## Slide 1: WF on CW update for Autonomous UL in FeLAA
CableLabs, Broadcom, Comcast, HPE
Charter Communications, Brocade, Blackberry
3GPP TSG RAN WG1 Meeting #91 R1- 1721072
Reno, Nevada, 27th Nov – 1st Dec 2017
Agenda item: 6.2.2.2.3

## Slide 2: Background (1)
In RAN1#90, the agreements made regarding Autonomous UL transmissions with Category 4 LBT included the following regarding the CW update mechanism:
  UE CW update procedure is the same as defined for Uplink Type 1 Channel access for eLAA [36.213, Section 15.2.2], except for possible availability of explicit HARQ feedback
    FFS: UE CW update based on HARQ feedback
This WF provides proposals to address the above FFS point regarding CW update based on HARQ feedback

## Slide 3: Background (2)
Principle: Any Category 4 LBT that begins a new COT should use a contention window size that captures the result of the transmissions in the previous COT (that started with Category 4 LBT).
This is also mandated by the ETSI BRAN regulation EN 301 893 (section 4.2.7.2.3.6) in the following way:
  1) The Channel Access Engine shall set CW to CWmin. 2) The Channel Access Engine shall select a random number q from a uniform distribution over the range 0 to CW
  ……………
  7) When the Channel Occupancy Time (COT) has completed, and it has been confirmed that at least one transmission that started at the beginning of the Channel Occupancy Time was successful, the Initiating Device proceeds with step 1) above otherwise the Initiating Device proceeds with step 8) below. 8) The Initiating Device may retransmit. If the Initiating Device does not retransmit the Channel Access Engine shall discard all data packets associated with the unsuccessful Channel Occupancy Time and the Channel Access Engine shall proceed with step 1) above. Otherwise the Channel Access Engine shall adjust CW to ((CW + 1) × m ) – 1. If the adjusted value of CW is greater than CWmax the Channel Access Engine may set CW equal to CWmax. The Channel Access Engine shall proceed with step 2) above

## Slide 4: Background (2)
However, LAA requires at least 4ms between a Category 4 LBT transmission and the indication of its result through HARQ feedback
Given this, the following exception can be made for AUL Category 4 LBT transmissions
  Between two AUL Category 4 LBT transmissions, there shall be a Contention window update if there was sufficient time to receive the feedback corresponding to the former Category 4 LBT transmission.

## Slide 5: Proposal (1)
The reference subframe is the first subframe of the most recent AUL burst of contiguous subframes that is transmitted after performing a category 4 LBT procedure with the following timing:
  At least 4 subframes prior to a UL grant reception or an AUL Downlink feedback information
The HARQ ID of the reference subframe is HARQ_ID_ref.

## Slide 6: Proposal (2)
Based on the UL grant content or/and AUL Downlink Feedback Information or the absence of either:
  The contention window size at the UE is reset for all the priority classes if:
  (1) the NDI bit for at least one of the active HARQ processes (i.e. TB not disabled) of HARQ_ID_ref in the reference subframe is toggled, OR
  (2) the AUL Downlink feedback information indicates ACK for at least one of the active HARQ processes (i.e. TB not disabled) of HARQ_ID_ref
  The contention window size of all priority classes at the UE is increased to the next higher value if:
  A UL grant is received and the NDI bit of the active HARQ processes of HARQ_ID_ref is not toggled ; OR
  A UL grant is received and does not schedule HARQ_ID_ref; OR
  An AUL Downlink feedback information is received and indicates NACK for the active HARQ processes (i.e. TB not disabled) of HARQ_ID_ref; OR
  A Category 4 LBT UL (SUL/AUL) transmission is initiated at least N subframes after the start of a previous Category 4 LBT UL(SUL/AUL) transmission without the reception of any UL grant or AUL Downlink Feedback Information in between, N = 6
  The CWS is reset to the minimum value if the maximum CWS is used for K consecutive LBT attempts for transmission only for the priority class for which maximum CWS is used for K consecutive LBT attempts.
    K is selected by UE implementation from the set of values from (1, …,8).