## Slide 1: WF on resource pool sharing between UEs using mode 3 and 4
LG Electronics, Qualcomm, ZTE
3GPP TSG RAN WG1 Meeting #91 R1-1721140
Reno, USA, November 27th – December 1st, 2017
Agenda item: 6.2.3.4

## Slide 2: Background
  The detailed objectives of WID on 3GPP V2X Phase 2 are as follows:
  Specify solutions for the following PC5 functionalities, which can co-exist in the same resource pools as Rel-14 functionality and use the same scheduling assignment format (which can be decoded by Rel-14 UEs), without causing significant degradation to Rel-14 PC5 operation compared to that of Rel-14 UEs: [RAN1, RAN2, RAN4]
    Carrier aggregation (up to 8 PC5 carriers);
    64QAM;
    Reduce the maximum time between packet arrival at Layer 1 and resource selected for transmission;
    Radio resource pool sharing between UEs using mode 3 and UEs using mode 4;

## Slide 3: Proposals
  When Rel-15 mode 3 UE performs SL SPS transmission, it sets “Resource reservation field of SCI format 1” to “SPS periodicity of associated SL SPS configuration”.
  FFS the necessity of other enhancements