## Slide 1: WF on Early data transmission
Huawei, HiSilicon, …
R1-1721175
3GPP TSG RAN WG1 Meeting #91
Reno, USA, November 27th – December 1st 2017
Agenda item 6.2.5.2

## Slide 2: Background
RAN2 Agreements in #99bis meeting
PRACH partitioning is used to indicate UE’s intention to use early data transmission in Msg3. Backward compatibility shall be preserved. FFS: details on the PRACH pool, e.g., preamble/time/frequency/carrier domain of PRACH partitioning.

## Slide 3: Proposals
  For early data transmission in Msg3:
    The UL grant in RAR is 20 bits for PRACH CEL 0 and PRACH CEL 1
    The UL grant in RAR is 12 bits for PRACH CEL 2 and PRACH CEL 3
  Maximum TBS for early data transmission in Msg3 is 1000 bits

## Slide 4: Proposals
  One reserved bit in MAC RAR is used to differentiate:
    UL grant in RAR for EDT
    UL grant in RAR for Non-EDT
  Depending on eNB’s implementation, PRACH partitioning can be based on preamble/time/frequency or its combination