## Slide 1: WF on NPRACH preamble format for single UL subframe
LG Electronics, Qualcomm, …
R1-1721179
3GPP TSG RAN WG1 Meeting 91
Reno, USA, November 27th – December 1st 2017
Agenda item 6.2.6.3.2

## Slide 2: Background
Since certain TDD cells may have much smaller cell coverage, the PRACH preamble format 4 is available in LTE TDD system.
If certain TDD cells, which support PRACH preamble format 4, operate the in-band mode or guard-band mode NB-IoT system, introducing the new NPRACH preamble format for short coverage has advantages on the latency and battery life on UE side.
Therefore, it is desirable considering new NPRACH preamble format for short coverage which supports similar cell coverage of PRACH preamble format 4 (e.g., 1.4 km).

## Slide 3: Background

## Slide 4: Background
Examples of NPRACH preamble format for short coverage in single UL SF
Example A
  CP length: 448 TS
  Symbol length: 8192 TS
  Number of back-to-back symbol groups (G): 2
  Maximum cell coverage: 1.48 km
  Available guard time: 13440 TS
Example B-1
  CP length: 448 TS
  Symbol length: 8192 TS
  Number of back-to-back symbol groups (G): 3
  Maximum cell coverage: 1.48 km
  Available guard time: 4800 TS
Example B-2
  CP length: 1572 TS
  Symbol length: 8192 TS
  Number of back-to-back symbol groups (G): 3
  Maximum cell coverage: 6.97 km
  Available guard time: 1428 TS

## Slide 5: Proposals
Following preamble parameters should be considered for NPRACH preamble format for single UL subframe in TDD NB-IoT system
  One CP length should be selected from [448] TS to [1572] TS
  The number of symbols (N) in the symbol group is 1
  The number of back-to-back symbol groups (G) in single UL subframe is 3
  The number of symbol groups (P) in the preamble is FFS
Preamble parameters of NPRACH preamble formats for 2 or 3 UL subframes in TDD NB-IoT system are FFS