## Slide 1: Way Forward on enabling and disabling of power saving signal for IDLE mode paging
Huawei, HiSilicon, ….
3GPP TSG RAN WG1 Meeting #91
RENO, USA, 27 November – 1 December 2017
Agenda item 6.2.6.1.1.2
R1-1721183

## Slide 2: Background
In RAN1#90bis, it was agreed:
Agreements:
RAN1 assumes that introduction of WUS does not alter PO/PF definition
At least in a UE’s DRX cycle:
  WUS supports at least being applied to all the UEs monitoring WUS associated to a PO in a cell NB-IoT carrier;
    FFS: eNB can configure WUS being applied to a group of more than one of the UEs associated to a PO in a cell NB-IoT carrier
    Send LS to request RAN2 input on feasibility of UE groups for WUS. (Xiaolei, HiSilicon, prepare draft LS in R1-1719102)
Working assumption:
At least in a UE’s DRX cycle, how the UE knows the WUS time location, is:
  A WUS has a time location which is configurable with respect to the associated PO(s) location(s)
Agreements:
At least in a UE’s DRX cycle, one WUS informs UE whether to monitor the PO in a single DRX cycle
Include in the LS to RAN2, to request input on the feasibility of WUS applying to more than one PO in a PTW for eDRX case

## Slide 3
Proposals:
The network can enable or disable use of the WUS for the whole cell through broadcast signaling;
A UE that is WUS-capable directly monitors the paging channel if the target coverage of the configured maximum duration of WUS is insufficient for the UE.
  FFS: how to inform the coverage information