## Slide 1: WF on Interpretation and application of subframes for additional SIB1-NB in FDD
LG Electronics, Ericsson, …
R1-1721186
3GPP TSG RAN WG1 Meeting 91
Reno, USA, November 27th – December 1st, 2017
Agenda item 6.2.6.2.2

## Slide 2: Background (agreement from RAN1#90bis)
SIB1-NB can be additionally transmitted in subframe(s) other than Rel.13 existing SIB1-NB transmission subframes on the anchor-carrier.
  [allocation-perspective]
    Additional SIB1-NBs are transmitted on subframe #3
    The periodicity of additional SIB1-NB transmissions is 20 ms and in the same radio frame as legacy transmission
    FFS the supported number(s) of additional transmissions of SIB1-NB
  [transmission-perspective]
    The TBS, coding, and modulation of additional SIB1-NB repetitions are the same as the existing ones for Rel.13 SIB1-NB
      FFS scrambling
    FFS: The sequence of coded bits-to-subframe allocation of additional SIB1-NB transmission can be interleaved compared to the existing SIB1-NB transmission
  [procedure-perspective]
    There is no signalling of the number of additional SIB1-NB transmissions
    Additional SIB1-NB transmission can be configured by eNB, and the presence of additional SIB1-NB can be indicated by one of unused bits in MIB-NB
      When additional SIB1-NBs are transmitted, the subframe(s) carrying additional SIB1-NB(s) can be declared as invalid downlink subframe by downlinkBitmap
        Rel.15 UEs interpret invalid downlink subframes whose indices are corresponding to additional SIB1-NBs transmissions but not carrying additional SIB1-NB (and NSSS) as valid downlink subframes
FFS if additional SIB1-NB transmissions are also supported on non-anchor carriers

## Slide 3: Background (NPDCCH)
Summary of NPDCCH
An NPDCCH search space is defined by a set of NPDCCH candidates where each candidate is repeated in a set of R consecutive NB-IoT downlink subframes excluding subframes used for transmission of SI messages starting with subframe k.
  The IE DL-Bitmap-NB is used to specify the set of NB-IoT downlink subframes for downlink transmission
*CBRA(Contention-based Random Access), **CFRA(Contention-free Random Access)

## Slide 4: Background (NPDSCH)
A UE shall upon detection on a given serving cell of a NPDCCH with DCI format N1, N2 ending in subframe n intended for the UE, decode, starting in n+5 DL subframe, the corresponding NPDSCH transmission in N consecutive NB-IoT DL subframe(s) ni with i = 0, 1, …, N-1 according to the NPDCCH information.
  The IE DL-Bitmap-NB is used to specify the set of NB-IoT downlink subframes for downlink transmission

## Slide 5: Proposals
Update the agreement from the RAN1#90bis meeting as follows
  When additional SIB1-NBs are transmitted, the subframe(s) carrying additional SIB1-NB(s) can be declared as invalid downlink subframe by downlinkBitmap
    Rel.15 UEs interpret invalid downlink subframes whose indices are corresponding to additional SIB1-NBs transmissions but not carrying additional SIB1-NB as valid downlink subframes only when the UE attempts to decode DCI format N0/N1 scrambled by C-RNTI in UE-specific search space or receive NPDSCH scheduled by DCI format N1 scrambled by C-RNTI in UE-specific search space.
    If the signaling in SIB1-NB to enable this feature is supported, it will be chosen from the following alternatives
      (Atl.1) using 1 bit to indicate whether the addition SF#3 that is configured but not used for SIB1-NBs can be used by Rel15 UEs.
      (Atl.2) using a 4-bits bit map to indicate in the Rel13/Rel14 bit map which SF#3 can be used for inband, and using a 1 bit for guardband and standalone.