## Slide 1: WF on Design of additional SIB1-NB in FDD
LG Electronics, ZTE, …
R1-1721187
3GPP TSG RAN WG1 Meeting 91
Reno, USA, November 27th – December 1st, 2017
Agenda item 6.2.6.2.2

## Slide 2: Background (agreement from RAN1#90bis)
SIB1-NB can be additionally transmitted in subframe(s) other than Rel.13 existing SIB1-NB transmission subframes on the anchor-carrier.
  [allocation-perspective]
    Additional SIB1-NBs are transmitted on subframe #3
    The periodicity of additional SIB1-NB transmissions is 20 ms and in the same radio frame as legacy transmission
    FFS the supported number(s) of additional transmissions of SIB1-NB
  [transmission-perspective]
    The TBS, coding, and modulation of additional SIB1-NB repetitions are the same as the existing ones for Rel.13 SIB1-NB
      FFS scrambling
    FFS: The sequence of coded bits-to-subframe allocation of additional SIB1-NB transmission can be interleaved compared to the existing SIB1-NB transmission
  [procedure-perspective]
    There is no signalling of the number of additional SIB1-NB transmissions
    Additional SIB1-NB transmission can be configured by eNB, and the presence of additional SIB1-NB can be indicated by one of unused bits in MIB-NB
    When additional SIB1-NBs are transmitted, the subframe(s) carrying additional SIB1-NB(s) can be declared as invalid downlink subframe by downlinkBitmap
      Rel.15 UEs interpret invalid downlink subframes whose indices are corresponding to additional SIB1-NBs transmissions but not carrying additional SIB1-NB (and NSSS) as valid downlink subframes
FFS if additional SIB1-NB transmissions are also supported on non-anchor carriers

## Slide 3: Background (code-rate of SIB1-NB)
TBS | Operation mode, (#CRS ports, #NRS ports) | # available REs in a subframe | Code rate | Portion of actual transmission of SIB-NB coded-bits over full SIB1-NB coded-bits
208 | Guard-band/Standalone, (NA,1) | 160 | 0.09 | 3.68
 | Guard-band/Standalone, (NA,2) | 152 | 0.1 | 3.49
 | In-band same/different PCI, (1,1) | 116 | 0.13 | 2.67
 | In-band same/different PCI, (2,2) or In-band different PCI (4,1) | 100 | 0.15 | 2.30
 | In-band different PCI, (1,1) | 92 | 0.16 | 2.11
328 | Guard-band/Standalone, (NA,1) | 160 | 0.14 | 2.42
 | Guard-band/Standalone, (NA,2) | 152 | 0.14 | 2.30
 | In-band same/different PCI, (1,1) | 116 | 0.19 | 1.76
 | In-band same/different PCI, (2,2) or In-band different PCI (4,1) | 100 | 0.22 | 1.52
 | In-band different PCI, (1,1) | 92 | 0.24 | 1.39
440 | Guard-band/Standalone, (NA,1) | 160 | 0.18 | 1.84
 | Guard-band/Standalone, (NA,2) | 152 | 0.19 | 1.75
 | In-band same/different PCI, (1,1) | 116 | 0.25 | 1.33
 | In-band same/different PCI, (2,2) or In-band different PCI (4,1) | 100 | 0.29 | 1.15
 | In-band different PCI, (1,1) | 92 | 0.32 | 1.06
680 | Guard-band/Standalone, (NA,1) | 160 | 0.28 | 1.21
 | Guard-band/Standalone, (NA,2) | 152 | 0.29 | 1.15
 | In-band same/different PCI, (1,1) | 116 | 0.38 | 0.88
 | In-band same/different PCI, (2,2) or In-band different PCI (4,1) | 100 | 0.44 | 0.76
 | In-band different PCI, (1,1) | 92 | 0.48 | 0.70

## Slide 4: Proposals (1/2)
For the repetition number 4 and 8, the total number of subframes for additional SIB1-NB transmission will be downselected between the following alternatives
  (Alt.1) no additional SIB1-NB transmission
  (Alt.2) half as many as that of the legacy SIB1-NB transmissions
  (Alt.3) the same as that of the legacy SIB1-NB transmissions
For the repetition number 16, the total number of subframes for additional SIB1-NB transmission will be downselected between the following alternatives
  (Alt.1) the same as that of the legacy SIB1-NB transmissions
  (Alt.2) depends on code rate (e.g., TBS, #CRS/NRS ports, operation mode) of SIB1-NB
    When the code rate of SIB1-NB is equal to or larger than X, additional SIB1-NB subframes are transmitted on every other subframe #3
    Otherwise, additional SIB1-NB subframes are transmitted on every 4th subframe #3
    If the total number of subframes for additional SIB1-NB transmission is less than that of the legacy SIB1-NB transmissions, the starting radio frame index of additional SIB1-NB transmission depends on Cell ID and the number of SIB1-NB repetition scheduled by MIB-NB

## Slide 5: Proposals (2/2)
The sequence of coded bits-to-subframe allocation of additional SIB1-NB transmission will be downselected between the following alternatives
  (Alt.1) The additional SIB1-NB uses the same coded bits-to-subframes mapping as the legacy SIB1-NB
  (Alt.2) reuse coded bits generated for existing SIB1-NB transmission while coded bits-to-subframe allocation is circularly shifted as much as 8 radio frames compared to the existing SIB1-NB transmission
  (Alt.3) the coded bits that are mapped to subframe #3 used for additional SIB1-NB transmissions are generated by continuing reading from the virtual circular buffer
Scrambling sequence will be generated and applied to subframes for additional SIB1-NB following one of the alternatives below
  (Alt.1) The additional SIB1-NB reuses the bit-level scrambling mechanism of legacy SIB1-NB, and uses the same symbol-level scrambling mechanism as NPBCH by replacing the initialization equation with
  (Alt.2) The scrambling sequence generator for additional SIB1-NB transmission is initialized with
  (Alt.3) The scrambling sequence used for the new SIB1-NB subframe is generated based on advancing the Gold sequence generators used for generating the scrambling sequence for SIB1-NB in subframe #4 in the same frame by 2560 shifts
  (Alt.4) Keep the same scrambling sequence as the legacy one if the additional SIB1-NB does not use the same coded bits-to-subframes mapping as the legacy SIB1-NB
Do not support additional SIB1-NB transmissions on non-anchor carrier