## Slide 1
3GPP TSG RAN WG1#91 R1-1721628
Reno, USA, November 27th – December 1st, 2017
Agenda item: 7.1.2.2
Offline Summary on Frequency Offset Indication for TDM Scenario where SS BW and RMSI BW are Confined within Minimum Carrier Bandwidth
Samsung

## Slide 2: Background
The frequency offset between the center/edge of SS/PBCH block and RMSI CORESET requires indication
With PRB grid offset indication (e.g. “floating sync”), one can assume the SS/PBCH block and RMSI CORESET are PRB level aligned.
This summary focuses on the scenario where the total bandwidth covering that of the SS/PBCH blocks and the initial active DL BWP containing RMSI CORESET when they occur in different time instances is confined within minimum carrier bandwidth
RAN4 agreed that the channel raster for <6 GHz is either 15 kHz or 100 kHz and the channel raster for >6 GHz is 60 kHz.
SS/PBCH block is assumed to be aligned on an SS raster
Min channel shifts by the granularity of a PRB level CH raster
RAN1 should strive for minimum number of configurations on the relative frequency location between SS/PBCH block and RMSI CORESET
Examples shown in this summary do not imply the corresponding combination of SS numerology, RMSI numerology and CORESET BW has to be supported

## Slide 3: Background
RAN4 Agreement on spectral utilization for below 6GHz (R4-1709075)
RAN4 Agreement on spectral utilization for above 6GHz (R4-1709075)

## Slide 4: Example 1
SS SCS = 15 kHz, CORESET SCS = 15 kHz, min CH BW = 5 MHz (25 PRBs for both SS and CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  3 configurations are sufficient to indicate the frequency offset

## Slide 5: Example 2
SS SCS = 15 kHz, CORESET SCS = 30 kHz, min CH BW = 5 MHz (25 PRBs for SS and 11 PRBs for CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 12 PRBs (in RMSI numerology)
  This scenario cannot be supported, unless the channel utilization of 5 MHz with 30 kHz can be at least 12 PRBs

## Slide 6: Example 3
SS SCS = 30 kHz, CORESET SCS = 15 kHz, min CH BW = 10 MHz (24 PRBs for SS, and 52 PRBs for CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset

## Slide 7: Example 4
SS SCS = 30 kHz, CORESET SCS = 30 kHz, min CH BW = 10 MHz (24 PRBs for both SS and CORESET)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  5 configurations are sufficient to indicate the frequency offset

## Slide 8: Example 5
SS SCS = 120 kHz, CORESET SCS = 60 kHz, min CH BW = 50 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset

## Slide 9: Example 6
SS SCS = 120 kHz, CORESET SCS = 120 kHz, min CH BW = 50 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 24 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset

## Slide 10: Example 7
SS SCS = 240 kHz, CORESET SCS = 120 kHz, min CH BW = 100 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 48 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset

## Slide 11: Example 8
SS SCS = 240 kHz, CORESET SCS = 60 kHz, min CH BW = 100 MHz (32 PRBs in SS numerology)
  SS/PBCH block BW = 20 PRBs (in SS numerology), RMSI CORESET BW = 96 PRBs (in RMSI numerology)
  2 configurations are sufficient to indicate the frequency offset

## Slide 12: Summary
The configuration of frequency offset for scenario, where the total bandwidth covering that of the SS/PBCH blocks and the initial active DL BWP containing RMSI CORESET when they occur in different time instances is confined within minimum carrier bandwidth, is summarized in the following table.
  Note: a = CORESET SCS / SS SCS in the table
SS SCS (kHz) | CORESET SCS (kHz) | CORESET BW (PRB in CORESET numerology) | # configurations of frequency offset | Center frequency offset value in PRB of CORESET numerology
15 | 15 | 24 | 3 | -2a, 0, 2a
15 | 30 | 12 | Not supported | 
30 | 15 | 48 | 2 | -a, a
30 | 30 | 24 | 5 | -2a, -a, 0, a, a
120 | 60 | 48 | 2 | -2a, 2a
120 | 120 | 24 | 2 | -2a, 2a
240 | 60 | 96 | 2 | -2a, 2a
240 | 120 | 48 | 2 | -2a, 2a