## Slide 1: WF on usage of Option B CQI table for efeMTC
Sony, Ericsson
3GPP TSG RAN WG1 Meeting #91 R1-1721226
Reno, Nevada, USA, November 27th – December 1st, 2017
Agenda item 6.2.5.5

## Slide 2: Background
The following agreements were made in RAN1#90bis (from chairman’s notes):
  RAN1 to design a solution to configure a UE with CSI reference resource comprising more than one subframe and 64QAM simultaneously.
  RAN1 to discuss the detailed solutions among the following options, where other options are not precluded:
    Option A: For csi-NumRepetitionCE-r13 > 1, the UE assumes a CSI reference resource of 1 for 64QAM and csi-NumRepetitionCE-r13 > 1 for other modulation schemes.
    Option B: Redesign CQI table to have a more even spread of SNR values.
Option B covers the whole SNR operating range from highest 64QAM code rate to lowest QPSK code rate with repetitions and does not require reconfigurations
The Option B CQI table avoids reconfiguration and is useful even when the UE is not configured with 64QAM

## Slide 3: Proposal
eNodeB can configure the UE to use the option B CQI table irrespective of whether 64QAM is configured or not