## Slide 1: WF on DMRS for transmit diversity
Ericsson, …
3GPP TSG RAN WG1 Meeting #92 R1-1803032
Athens, Greece, 26th March – 2nd March 2018
Agenda item – 6.2.3.3.1

## Slide 2: Background
From RAN1#91
Assuming the previous WA of introducing non-transparent transmit diversity is confirmed, for two-port non-transparent transmit diversity for PSSCH, downselect option 1 as WA among the following candidate schemes
  Working assumption: Option 1: SFBC-based scheme (including PAPR preserving)
    FFS whether to apply slot-level PVS
  Option 2: STBC-based (including half symbol)

## Slide 3: Background
From RAN1#88bis:
Agreement:
  When only one antenna port is applied, legacy DMRS pattern is reused.
  For the case that more than one antenna port is applied, the time location of DMRS is the same as Rel-14.
  Channel estimation and demodulation details should be provided by proponents
  There should be analysis on impact to Rel-14 UE provided following with evaluation assumption and link and/or system simulations, including interference increase of Rel-15 UEs over Rel-14 UEs
    Details FFS

## Slide 4: Background
From RAN1#89 [3] :
Legacy Rel-14 DMRS pattern with single antenna port, including time-frequency location, sequence, and cyclic shift, is applied to PSCCH transmission.

## Slide 5: Background
From R1-1801310, “LS reply on transmit diversity impact on V2X PC5,” RAN4:
A. Impact on PSSCH-RSRP measurement accuracy of Rel-14 UEs
Answer: RAN4 concluded that introduction of two-port non-transparent transmit diversity schemes in Rel-15 may lead to the impact on Rel-14 V2X UEs PSSCH-RSRP measurements accuracy. The impact depends on the two port DMRS design.
If Rel-15 two-port PSSCH DMRS does not include legacy Rel-14 DMRS sequence, Rel-14 UE will fail to perform PSSCH-RSRP measurements.
If Rel-15 two-port PSSCH DMRS includes legacy Rel-14 DMRS sequence, Rel-14 UE PSSCH-RSRP accuracy will degrade:
  For one type of PSSCH-RSRP measurement algorithm:
    -3 dB RSRP power offset will be observed comparing to the total RX power from the two DMRS APs.
    Almost no RSRP bias will be observed comparing to the RSRP from one antenna port.
    The variance of RSRP estimates may increase due to presence of interference from the second DMRS AP. Based on observation from some companies, the increase is limited.
  For a certain Rel-14 V2X UE implementation, it is observed that PSSCH-RSRP measurement is significantly impacted with certain DMRS designs. For some other DMRS design, the observed impact is the same as the first type of PSSCH-RSRP measurement algorithm.
  The impact on the resource selection and overall V2X performance is up to RAN1
  Note: RAN4 does not specify the PSSCH-RSRP estimation algorithm and it is left up to UE implementation.

## Slide 6: Proposal
DMRS for PSSCH using non-transparent transmit diversity:
First antenna port:
  Rel-14 DMRS sequence is transmitted in OFDM symbols #2 and #8
  Rel-14 DMRS sequence with SFBC precoding is transmitted in OFDM symbols #5 and #11
Second antenna port:
  Rel-14 DMRS sequence is transmitted in OFDM symbols #5 and #11
  Rel-14 DMRS sequence with SFBC precoding is transmitted in OFDM symbols #2 and #8
Note: OFDM symbols are numbered #0 to #13