## Slide 1
3GPP TSG RAN WG1 Meeting #92 R1-1803046
Athens, Greece, February 26th – March 2nd, 2018
Agenda item: 6.2.6.1.1.3
WF on WUS Sequence Design
Qualcomm, Samsung, LGE, ZTE, SaneChips

## Slide 2: Background
Working assumption
WUS sequence is a sequence mapping within one subframe as a basic unit and repeated/extended for multiple subframes to support larger coverage.
  prioritize to minimize impact on UE synchronization performance.
FFS: detailed design on time-varying of the WUS signal
Agreement
UE can assume all the REs for transmission of WUS in a given subframe use the same antenna port.
The UE shall not assume the transmission of WUS in more than X consecutive subframes use same antenna port.
  FFS: value of X
WUS sequence is based on ZC-sequence
  When designing WUS sequence, negative impact on legacy NSSS detection should be avoided.

## Slide 3: Proposal
Confirm working assumption:
  WUS sequence is a sequence mapping within one subframe as a basic unit and repeated/extended for multiple subframes to support larger coverage.
    prioritize to minimize impact on UE synchronization performance.
WUS sequence is a NSSS-like sequence as
  FFS RE-based cover codes c(m) using
    Hadamard codes
    Gold sequences
    M sequences
  FFS phase shift
  FFS time-varying design
In every subframe mapped with WUS sequence, the number of WUS sequences is at least 504, and every cell ID corresponds to at least one unique WUS sequence.
  FFS: whether WUS sequence is generated also based on UE group ID or other information.
,