## Slide 1
Ericsson, ..

## Slide 2: HARQ bitmap field in AUL-DFI
Ericsson
R1-1803048
3GPP TSG RAN1 #92
Athens, Greece, Feb 26– Mar 2 2018
Agenda item 6.2.2.2

## Slide 3: background
  Agreement from Meeting #90bis
AUL downlink feedback information ("AUL-DFI") is specified to carry at least AUL HARQ feedback
  Bitmap with one HARQ-ACK-bit for each AUL-configured HARQ process per TB (FFS: whether spatial bundling is used)
    The HARQ feedback includes pending feedback for several uplink transmissions from the same UE.
  Agreement from Meeting #90bis
  AUL-DFI shall contain HARQ-ACK feedback for SUL transmissions using AUL-enabled HARQ IDs
    AUL is not allowed for SUL retransmission

## Slide 4: Background
Herein, we consider a case where the reference subframe corresponding to AUL-DFI is “pure” SUL (i.e., with HARQ ID not configured for AUL)
In pure scheduling scenario the eNB indicates (explicitly or implicitly) ACK/NACK of the reference subframe. The UE will not initiate a CAT4 LBT, if a new UL grant is not received.
In a mixed SUL/AUL scenario, if the UE wants to initiate an AUL CAT4 LBT and the reference subframe is a pure SUL HARQ, the UE needs to double the contention window if the eNB fails to reschedule the same HARQ id within a certain time.
  so even if the transmission was successful, the eNB needs to reschedule the UE using same HARQ with NDI toggled to indicate to the UE a successful transmission. Even though the idea of AUL is to avoid a lot of scheduling occasions.

## Slide 5: Background
To avoid this case, we suggest that the bit map in the AUL-DFI includes all the HARQ ids (common between AUL/SUL and SUL only).
Therefore, the eNB has the flexibility to ACK/NACK an SUL-only HARQ via two means:
  UL grant
  Explicit indication in AUL-DFI

## Slide 6: Proposal
HARQ-Ack bitmap in AUL-DFI:
  AUL TM1: 16 bits (one HARQ-ACK-bit for each UL HARQ process)
  AUL TM2: 32 bits (one HARQ-ACK-bit for each UL HARQ process per TB)
AUL-DFI shall contain HARQ-ACK feedback for SUL transmissions
    AUL is not allowed for SUL retransmission