## Slide 1: Summary on Tx Diversity
Huawei
3GPP TSG RAN WG1 Meeting #92 R1-1813100
Athens, Greece, February 26 – March 2, 2018
Agenda item: 6.2.3.3

## Slide 2: Background
There is therefore not consensus to confirm the working assumption to adopt non-transparent tx diversity, due to concerns on the impact on Rel-14 UEs with IRC receivers
Until Thursday: Work offline to identify an alternative way forward – Philippe (Huawei)
e.g. CDD based TxD, or a way of mitigating the impact on Rel-14 UEs.

## Slide 3: Proposal
Option 1: SFBC-based transmit diversity for PSSCH shall not be used if the ratio of resources containing decoded PSCCH Rel-14 transmissions and/or not indicating SFBC-based transmit diversity transmission to the total number of resources is above a (pre-)configured threshold for that pool.
  Setting the threshold to 0 prevents altogether the use of non-transparent transmission diversity in the pool.
  When SFBC-based transmit diversity is not used, CDD can be used
Option 2: CDD can be used. SFBC-based transmit diversity not specified