## Slide 1: WF on All remaining issues on system acquisition latency enhancement
LG Electronics, Ericsson, [Huawei], [HiSilicon]
R1-1803103
3GPP TSG RAN WG1 Meeting 92
Athens, Greece, February 26th – March 2nd, 2018
Agenda item 6.2.6.2.2

## Slide 2: Background (additional SIB1-NB)
For the repetition number 4 and 8, the total number of subframes for additional SIB1-NB transmission will be downselected between the following alternatives
  (Alt.1) no additional SIB1-NB transmission
  (Alt.2) half as many as that of the legacy SIB1-NB transmissions
  (Alt.3) the same as that of the legacy SIB1-NB transmissions
For the repetition number 16, the total number of subframes for additional SIB1-NB transmission will be downselected between the following alternatives
  (Alt.1) the same as that of the legacy SIB1-NB transmissions
  (Alt.2) depends on code rate (e.g., TBS, #CRS/NRS ports, operation mode) of SIB1-NB
    When the code rate of SIB1-NB is equal to or larger than X, additional SIB1-NB subframes are transmitted on every other subframe #3
    Otherwise, additional SIB1-NB subframes are transmitted on every 4th subframe #3
    If the total number of subframes for additional SIB1-NB transmission is less than that of the legacy SIB1-NB transmissions, the starting radio frame index of additional SIB1-NB transmission depends on Cell ID and the number of SIB1-NB repetition scheduled by MIB-NB

## Slide 3: Background (additional SIB1-NB)
The sequence of coded bits-to-subframe allocation of additional SIB1-NB transmission will be downselected between the following alternatives
  (Alt.1) The additional SIB1-NB uses the same coded bits-to-subframes mapping as the legacy SIB1-NB
  (Alt.2) reuse coded bits generated for existing SIB1-NB transmission while coded bits-to-subframe allocation is circularly shifted as much as 8 radio frames compared to the existing SIB1-NB transmission
  (Alt.3) the coded bits that are mapped to subframe #3 used for additional SIB1-NB transmissions are generated by continuing reading from the virtual circular buffer
Scrambling sequence will be generated and applied to subframes for additional SIB1-NB following one of the alternatives below
  (Alt.1) The additional SIB1-NB reuses the bit-level scrambling mechanism of legacy SIB1-NB, and uses the same symbol-level scrambling mechanism as NPBCH by replacing the initialization equation with
  (Alt.2) The scrambling sequence generator for additional SIB1-NB transmission is initialized with
  (Alt.3) The scrambling sequence used for the new SIB1-NB subframe is generated based on advancing the Gold sequence generators used for generating the scrambling sequence for SIB1-NB in subframe #4 in the same frame by 2560 shifts
  (Alt.4) Keep the same scrambling sequence as the legacy one if the additional SIB1-NB does not use the same coded bits-to-subframes mapping as the legacy SIB1-NB

## Slide 4: Background (NPBCH/MIB-NB)
Other remaining issues in NPBCH and MIB-NB skipping
  Whether or not to introduce new repetitions for NPBCH
  Whether or not to use additional information in direct indication/SI modification to enable MIB skipping

## Slide 5: Proposals
[for additional SIB1-NB]
  For the repetition number 4 and 8, the following alternative is downselected for the total number of subframes for additional SIB1-NB transmission
    no additional SIB1-NB transmission
  For the repetition number 16, the following alternative is downselected for the total number of subframes for additional SIB1-NB transmission
    the same as that of the legacy SIB1-NB transmissions
  The following alternative is downselected for the sequence of coded bits-to-subframe allocation of additional SIB1-NB transmission
    the coded bits that are mapped to subframe #3 used for additional SIB1-NB transmissions are generated by continuing reading from the virtual circular buffer
  The following alternative is downselected for the scrambling sequence applied to subframes for additional SIB1-NB
    Keep the same scrambling sequence as the legacy one
[for NPBCH]
  Do not introduce new NPBCH repetitions
[for MIB-NB skipping]
  Send LS to RAN2 to recommend the study of skipping MIB-NB decoding mechanisms
    “From RAN1 point of view, SI acquisition latency reduction after SI modification indication is expected if the UE can skip MIB-NB decoding, e.g., by using Direct indication information field in the DCI format N2 scrambled by P-RNTI. ”