## Slide 1: WF on group based beam reporting
3GPP TSG RAN WG1 Meeting #92 R1-1803281
Athens, Greece, February 26th – March 2nd, 2018
Agenda Item: 7.1.2.2.3
ZTE, Sanechips, vivo, NTT DOCOMO, OPPO, Samsung, Huawei, HiSilicon, LGE, Mitsubishi Electric, Intel, ASTRI, [Nokia, NSB, CATT, Ericsson, MediaTek, Qualcomm]

## Slide 2: Background
Agreements:
Support the following for group based beam reporting, if group based beam reporting is configured:
  In a beam reporting instance, a UE can be configured to report N different Tx beams that can be received simultaneously
    Note: UE may report N or fewer beams in a given reporting instance
    N is configured by the gNB where N<= Nmax
      Nmax depends on UE capability
        FFS: how to define the UE capability
        N =2 is supported. Further study {4,8}
      Notes: Information indicating group is not required to be reported in Rel-15
  Note:
    From the perspective of Alt-1, the UE reports one group with N Tx beams.
    From the perspective of Alt-2, the UE reports N group with one Tx beam per each group.
  Note: Mechanisms to reduce UE complexity for beam pair search should be further studied

## Slide 3: Proposal: Beam reporting
  Proposal: In beam reporting, NR supports the following aspects:
    The reporting format of differential L1-RSRP for non-group based beam reporting is reused for group based beam reporting.
      Support UE to report its capability of maximum number of reported beams for group based beam reporting, and its candidate value is {1, 2}.